## Slide 1
A DC-100 GHz Bandwidth and 20.5 dB Gain
Limiting Amplifier in 0.25μm InP DHBT Technology
Saeid Daneshgar, Prof. Mark Rodwell (UCSB)
Zach Griffith (Teledyne Scientific Company)

## Slide 2: Outline
Application and Motivation of the work
TSC 250nm HBT process overview
Block diagram & schematic of the circuit
Layout & EM modeling
Measurement results and comparison table

## Slide 3: Motivation - I
50 GSample/sec Sample & Hold circuit

## Slide 4: Motivation - II
50 GHz clock circuit

## Slide 5: Applications - I
High speed optoelectronic signal conversion requires broadband receivers
Limiting amplifiers are the key components in these receivers in order to:
Provide a low input sensitivity and sufficient gain to achieve saturated output levels from small-signal inputs which enables reliable decision making
Provide a wide bandwidth to achieve short rise and fall times in order to provide an output signal with minimum distortion

## Slide 6: TSC 250nm InP HBT process
Four metal interconnect stack
Peak bandwidth of ft=400 GHz & fmax = 700 GHz
MIM caps of 0.3 fF/μm2
Thin-film resistors 50 Ω/square
Plot courtesy Zach Griffith, UCSB 250nm InP HBT, 2007

## Slide 7: Modified Cherry-Hooper stage [1-3]
[1] Y. M. Greshishchev et al., “A 60-dB gain, 55-dB dynamic range, 10-Gb/s broad-band SiGe HBT limiting amplifier,” IEEE JSSC, vol.34, no.12, pp. 1914-1920, Dec. 1999.
[2] K. Ohhata et al., “Design of a 32.7-GHz bandwidth AGC amplifier IC with wide dynamic range implemented in SiGe HBT,” IEEE JSSC, vol.34, no.9, pp. 1290-1297, Sep. 1999
[3] C. D. Holdenried et al., “Analysis and design of HBT Cherry-Hooper amplifiers with emitter-follower feedback for optical communications,” IEEE JSSC, vol.39, no.11, pp. 1959-1967, Nov. 2004.
Large signal behavior:
Conventional C-H amp. gain ≈ gm1-2 RF
Modified C-H amp. provides gain enhancement by a factor of while 0 < < 2.5

## Slide 8: Block Diagram
Single-ended gain and BW measurements have be chosen due to unavailability of 4-port s-param measurement for frequencies > 67 GHz → ~6dB gain has been added to get the differential equivalent

## Slide 9: Schematic
R1 =30 Ω
R2 =50 Ω
RF =40 Ω
Q1-8 =3x0.25 μm

## Slide 10: Compact layout
425 µm
500 µm
140 µm
100 µm

## Slide 11: Symmetric layout

## Slide 12: EM Simulation
54 port data item
Whole chip has been modeled using ADS momentum EM simulator

## Slide 13: S-parameter measurement results - I
Single-ended insertion loss
Single-ended input and output return loss
S21=14.5 dB , 3dB BW = 100 GHz
S21 gain ripple < ±0.5 dB
S11< -20 dB , S22< -15 dB

## Slide 14: S-parameter measurement results - II
Rollet Stability factor
Group Delay
Group delay ≈ 9 psec
Group delay variation = 11 psec

## Slide 15: Eye diagrams @ 30 Gb/s
Small Signal
Large Signal

## Slide 16: Eye diagrams @ 40 Gb/s
Small Signal
Large Signal

## Slide 17: Comparison table

## Slide 18: Thank you for your listening