## Slide 1: An 81 GHz, 470 mW, 1.1 mm2 InP HBT Power Amplifier with 4:1 Series Power Combining using Sub-quarter-wavelength Baluns
H. Park1, S. Daneshgar1, J. C. Rode1, Z. Griffith2, M. Urteaga2, B.S. Kim3, M. Rodwell1
1University of California, Santa Barbara, CA, US
2Teledyne Scientific and Imaging, Thousand Oaks, CA, US
3Sungkyunkwan University, Suwon, Republic of Korea
TU3B-1
Student
Paper
Finalist

## Slide 2: Outline
2
Motivation, Challenge
Power-combining Techniques in mm-Wave
Proposed Baluns (2:1 and 4:1 Series Combiners)
Power Amplifier Designs (2:1 and 4:1)
Measurement Results and Comparisons
Conclusion
TU3B-1
IMS2014, Tampa, 1-6 June, 2014

## Slide 3: mm-Wave Power Amplifier: Challenges
mm-Wave PAs: Applications: High speed communications, high resolution images
Needed: High power / High efficiency / Small die area (low cost)
3
Extensive power combining
Compact power-combining
Efficient power-combining
Class E/D/F are poor @ mm-wave insufficient gain ~fmax, high losses in harmonic terminations
Goal: efficient, compact mm-wave power-combiners
TU3B-1
IMS2014, Tampa, 1-6 June, 2014

## Slide 4: Parallel Power-Combining
4
Output power: POUT = V x (M x I) Parallel connection increases POUT
Load Impedance: ROPT = V / (M x I) Parallel connection decreases ROPT
High POUT using low VDD  Low ROPT
Needs impedance transformation: Wilkinson or lumped lines …
High insertion loss
Small bandwidth
Large die area
TU3B-1
IMS2014, Tampa, 1-6 June, 2014

## Slide 5: Series Power-Combining & Stacks
5
Local voltage feedback: drives gates, sets voltage distribution
Design challenge: need uniform RF voltage distribution need ~unity RF current gain per element
...needed for simultaneous compression of all FETs.
Parallel connections: IOUT = M x I Series connections: VOUT = N x V
Output power: POUT = (N·M) x V x I Load impedance: ROPT = (N/M) x V/I Small or zero power-combining losses
Small die area BUT, how do we drive the gates ?
TU3B-1
IMS2014, Tampa, 1-6 June, 2014

## Slide 6: Proposed l/4 Baluns
6
Our proposed balun with l/4 lines Three-conductor transmission-lines
 Two separate transmission lines (m3-m2, m2-m1)
Fields between m3 and m1 isolated!
l/4 line stub → Zstub = open BUT, still long line → high loss and large die area 
Balun structure
Simplified model
TU3B-1
IMS2014, Tampa, 1-6 June, 2014

## Slide 7: Proposed Sub-l/4 Baluns
7
What if balun length is << l/4 ?  Stub line becomes inductive!
Sub-l/4 balun: Inductive stub line Tunes transistor COUT !! Short line → Low losses  → Small die area 
*Symbol:
Three-conductor transmission line
TU3B-1
IMS2014, Tampa, 1-6 June, 2014

## Slide 8: Ideal Tri-axial Line
Two separate transmission lines (m3-m2, m2-m1)
 E, H fields between m3 and m1 perfectly shielded
TU3B-1
IMS2014, Tampa, 1-6 June, 2014

## Slide 9: Baluns in Real ICs
9
  1) M1 as a GND
  2) Slot-type transmission lines (M1-M2), AC short (2 pF MIM)
  3) Microstrip line (M2-M3), E-field shielding NOT negligible
  4) Sidewalls between M3-M1 (Faraday cages), l/16 length
1)
2)
3)
4)
TU3B-1
IMS2014, Tampa, 1-6 June, 2014

## Slide 10: 2:1 Balun B-to-B Test Results
10
*Does not de-embed losses of PADs , capacitors, and interconnection lines
Back-to-back measured S-parameters
CP = 103fF
FC = 81GHz
I.L. = -1.1dB
S21 = -1.76dB
CP = 78fF
FC = 94GHz
I.L. = -1.2dB
S21 = -1.79dB
CP = 65fF
FC = 103GHz
I.L. = -1.2dB
S21 = -1.56dB
v1
v2
v3
< 0.6dB single-pass insertion loss, 0.16 dB/2.7° imbalance
TU3B-1
IMS2014, Tampa, 1-6 June, 2014

## Slide 11: Teledyne 0.25 μm HBTs
11
Cell: 4-fingers x 0.25 μm x 6 μm
BVCEO = 4.5 V, IC,max = 72 mA
POUT = 15.5 dBm
ROPT = 56 Ω
MAG/MSG including EM-Sim. results
fτ =285 GHz, fmax =525 GHz
@ JE =4.2 mA/μm2 and VCE =2.5 V
12~13dB MAG @ 86 GHz
Base
Emitters to GND
Collector
[Z. Griffith et al, IPRM 2012] Multi-finger 250nm InP HBTs for 220GHz mm-Wave Power Multi-finger 250nm InP HBTs for 220GHz mm-Wave Power
TU3B-1
IMS2014, Tampa, 1-6 June, 2014

## Slide 12: Sub-l/4 Baluns: PA Design
12
Each HBT loaded by 25 W HBT junction area selected so that Imax=Vmax/25 W
Each HBT has some COUT Stub length picked so that Zstub=-1/jwCOUT → tunes HBT
4:1 more power than without the combiner.
TU3B-1
IMS2014, Tampa, 1-6 June, 2014

## Slide 13: 4:1 PA Designs Using 2:1 Balun
13
Identical input / output baluns
2-section LC input matching network
Active bias: Thermal stability & class-AB
IC size: 450 x 820 um2
[H. Park et al, CSICS 2013] 30% PAE W-Band InP Power Amplifiers Using Sub-Quarter-Wavelength Baluns for Series-Connected Power-Combining
TU3B-1
IMS2014, Tampa, 1-6 June, 2014

## Slide 14: Single-Stage PA IC Test Results (86GHz)
14
  Gain: 10 dB
  PSAT: >100 mW @2.5V
  PAE: >30 %
  3-dB BW: 23 GHz
  Power density (power/die area)
  = 294 mW/mm2 (including RF pads) = 1210 mW/mm2 (core area)
Small signal measurements
Large signal measurements
[H. Park et al, CSICS 2013] 30% PAE W-Band InP Power Amplifiers Using Sub-Quarter-Wavelength Baluns for Series-Connected Power-Combining
TU3B-1
IMS2014, Tampa, 1-6 June, 2014
x4 larger output power
than 50 Ohm ROPT device

## Slide 15: Two-Stage PA IC Test Results (86GHz)
15
  Gain: 17.5 dB
  PSAT: >200 mW @ 3.0 V
  PAE: >30 %
  Power density (power/die area)
  = 307 mW/mm2 (including RF pads) = 927 mW/mm2 (core area)
Large signal measurements
  IC size: 825 x 820 um2
[H. Park et al, CSICS 2013] 30% PAE W-Band InP Power Amplifiers Using Sub-Quarter-Wavelength Baluns for Series-Connected Power-Combining
TU3B-1
IMS2014, Tampa, 1-6 June, 2014

## Slide 16: 16:1 PA Using 4:1 Baluns
16
  4:1 series-connected power-combining
Each HBT has some COUT Stub length picked so that Zstub=-1/jwCout → tunes HBT
16:1 more power than without combiner.
Each HBT loaded by 12.5W HBT junction area selected so that Imax=Vmax/12.5W
TU3B-1
IMS2014, Tampa, 1-6 June, 2014

## Slide 17: PA IC Schematic (2-stages)
17
  2-stage PA using 2:1 and 4:1 baluns
1st stage
2nd stage
Long lead lines
Zload ≠ Z’load
TU3B-1
IMS2014, Tampa, 1-6 June, 2014

## Slide 18: PA IC Die Image (2-stages)
18
  IC Size: 1.08 x 0.98 mm2
TU3B-1
IMS2014, Tampa, 1-6 June, 2014

## Slide 19: PA IC Test Results (81 GHz)
19
  Gain: 17.8dB
  Output Power: 470mW @2.75 V
  PAE: 23.4%
  Power density (power/die area)
  = 443 mW/mm2 (including pads) = 1020 mW/mm2 (only core area)
Small signal measurements
Large signal measurements
TU3B-1
IMS2014, Tampa, 1-6 June, 2014
x16 larger output power
than 50 Ohm ROPT device

## Slide 20: mm-Wave Power Combiners
20
Ref. | Tech. | Type | N-way | Freq. (GHz) | IL (dB) | Size (mm2)
This work | 0.25 μm InP HBT | Sub-l/4 TL | 2:1 | 86 (60-105) | 0.52 (0.68) | 0.03
This work | 0.25 μm InP HBT | Sub-l/4 TL (ring) | 2:1 | 86 (60-110) | 0.50 (0.63) | 0.04
This work | 0.25 μm InP HBT | Sub-l/4 TL | 4:1 | 87 (75-103) | 0.91 (1.32) | 0.06
2012 Yi | 0.13 μm BiCMOS | TF | 4:1 | 60 77/79 | 0.73* 1.20* | 0.015
2013 Thian | 0.18 μm BiCMOS | TF | 8:1 | 83.5 (70.5-85) | 1.25 (0.80*) | 0.02#
2010 Chen | 65 nm CMOS | TF | 4:1 | 60 | 0.63* | 0.02#
2010 Law | 90 nm CMOS | Wilkinson | 2:1 | 60 | 0.54 | 0.08
2014 Zhao | 40 nm CMOS | Series/ parallel TF | 4:1 | 75 (65-90) | 0.92* (1.0) | 0.05#
2007 Niknejad | 90 nm CMOS | TL | 4:1 | 60 (55-65) | 1.09* (1.25*) | -
2007 Liu | 0.18 μm CMOS | Marchand | 2:1 | 57 | 3.40 | 0.55
2005 Hamed | InGaP/GaAs | Marchand | 2:1 | (15-45) | (1.50) | 0.40
*Simulation results, #Area estimated by chip image. IL: insertion loss, TF: transformer, and TL: transmission-line. Parentheses in the frequency and insertion loss columns indicate worst-case insertion loss over the indicated bandwidth. |  |  |  |  |  | 
TU3B-1
IMS2014, Tampa, 1-6 June, 2014

## Slide 21: mm-Wave Power Amplifiers
21
Ref. | Tech. fmax / ft (GHz) | Freq. (GHz) | BW (GHz) | Max. S21 (dB) | Pout (dBm) | Peak PAE (%) | VCC or VDD (V) | Size (mm2) | mW /mm2
This work | 0.25 μm InP HBT 525 / 285 | 86 | 23 | 9.4 | 20.4 | 30.4 | 2.5 | 0.37 0.09* | 294 1210*
This work | 0.25 μm InP HBT 525 / 285 | 86 | 33 | 10.2 | 20.8 | 35.0 | 2.5 | 0.43 0.14* | 285 858*
This Work | 0.25 μm InP HBT 525 / 285 | 81 | >11.5 | 17.5 | 26.7 | 23.4 | 2.75 | 1.06 0.46* | 443 1020*
2011 Brown | 0.14 μm GaN HEMT | 91 | 7+ | 16.0 | 30.8 | >20.0 | 17.5 | 2.25 | 530
2012 Micovic | 0.14 μm GaN HEMT 230 / 97 | 95 | 10+ | 18.0+ | 31.5+ | 20.5+ | 12.0 | - | -
2012 Yi | 0.13 μm BiCMOS 270 / 240 | 62 84 | >10 >8 | 20.6 27.0 | 20.1 18.0 | 18.0 9.0 | 1.8 2.5 | 0.72 0.68 | 142 93
2013 Agah | 45 nm SOI CMOS | 89 | 10+ | 10.3 | 15.8 | 11.0 | 2.8 | 0.37 0.05* | 103 760*
2013 Thian | 0.18 μm BiCMOS 250 / 170 | 78 | 8.9 | 18.3 | 14 | 2.0 | 3.2 | 0.85* | 29*
2010 Chen | 65nm CMOS | 60 | 9 | 20.3 | 18.6 | 15.1 | 1.0 | 0.28* | 256*
2010 Law | 90nm CMOS | 60 | 8 | 20.6 | 19.9 | 14.2 | 1.2 | 1.76 | 55
2014 Zhao | 40nm CMOS | 80 | 15.2 | 18.1 | 20.9 | 22.3 | 0.9 | 0.19* | 647*
*IC core area (excluding DC feed lines and RF pads), +Value estimated from figure, c)Corporate transmission-line power-combiners, s)Stacked PA. |  |  |  |  |  |  |  |  | 
TU3B-1
IMS2014, Tampa, 1-6 June, 2014

## Slide 22: Conclusion
22
Sub-l/4 baluns for series-power-combining using a low VBV device Low-loss <0.6dB @ 2:1 balun, <0.92dB loss @ 4:1 balun  High power, high efficiency, compact PA IC designs
W-band power amplifiers using the 2:1 & 4:1 baluns Record >30 % PAE @ 100 mW, 200 mW, 23.4 % PAE @470 mW Record 23 GHz 3-dB bandwidth, >10GHz 3-dB BW Record 1210 mW/mm2 power density, 1020 mW/mm2
Future directions 220GHz PA designs using the sub-l/4 baluns SiGe PA designs with the optimized balun structures Phased arrays at K/V/E/W bands
TU3B-1
IMS2014, Tampa, 1-6 June, 2014

## Slide 23: Thanks for your attention!
23
TU3B-1
IMS2014, Tampa, 1-6 June, 2014
hcpark@ece.ucsb.edu