## Slide 1
A 140GHz power amplifier with 20.5dBm output power and 20.8% PAE in 250-nm InP HBT technology
A. Ahmed1, M. Seo2, A. Farid1, M. Urteaga3, J. Buckwalter1, and M. Rodwell1
1University of California at Santa Barbara, CA, USA
2Sungkyunkwan University, South Korea
3Teledyne Scientific and Imaging, Thousand Oaks, CA, USA

## Slide 2: mm-wave Communication (140-1000 GHz)
Objective
  Support high data rate communication.
  Spatial multiplexing for high capacity.
  Cover long distance.
Benefits (140- 1000 GHz)
  Large available spectrum, high data rate.
  Shorter 𝜆: more channels for the same array size.
Challenge
  Atmospheric attenuation is high

## Slide 3: PA Requirments and Link Budget
CMOS chips drives high efficiency InP power amplifiers
CMOS’s output power is ~2dBm
20.5dBm output power per element extends the link range to ~50m
Required gain ~20dB
Massive MIMO arrays requires high efficiency PAs to avoid thermal destruction or complex heatsink
Tx Antenna Gain | 22.7 dBi
Rx Antenna Gain | 13 dBi
Link range | 50 m
Required output power per element | 20.5dBm
Friss Path Loss | 73 dB
Rx Noise Figure | 8.5 dB
Rx BW | 5 GHz
Bit rate | 10 Gb/s
System Margin | 15 dB
No of elements, Tx ( spacing) | 32
No of elements, Rx ( spacing) | 4
Tx Antenna Gain | 22.7 dBi
Rx Antenna Gain | 13 dBi
Link range | 50 m
Required output power per element | 20.5dBm
Friss Path Loss | 73 dB
Rx Noise Figure | 8.5 dB
Rx BW | 5 GHz
Bit rate | 10 Gb/s
System Margin | 15 dB
 | 32
 | 4
calculated data are based on
https://www.ece.ucsb.edu/Faculty/rodwell/Classes/ece218c/ECE218c.htm

## Slide 4: 250nm InP HBT Process (Teledyne*)
fmax=650GHz.
BVCEo=4.5V.
Jmax=3mA/µm.
Four Au interconnect.
MIM cap (0.3fF/µm2).
TFR (50Ω/square).
*M. Urteaga, et al, Proc. IEEE, June 2017.
Plot courtesy Zach Griffith, UCSB 250nm InP HBT, 2007

## Slide 5: Unit Cell Comparison
Comparison between CE, grounded CB and CB with base capacitor
Simulation is done under same bias condition
Large signal simulation is more relevant in power amplifier
CB with base capacitor shows the highest OP1dB with associated PAE
 | Gain*, dB | PAE**, % | Pout**, dBm
CE | 10.7 | 15.4 | 12.0
Grounded CB | 13.1 | 22.4 | 13.5
CB with 600 cap | 9.8 | 29.7 | 15.2
At 140GHz
*under opt load line condition without compression **at 1dB gain compression
Pout, gain, and PAE for CE, grounded CB, and CB with base capacitor.
(a) CE
(b) CB with grounded base
(c) CB with base capacitor

## Slide 6: Unit Cell Comparison
Common emitter
  Lowest OP1dB and Soft compression
  Less sensitive to base inductance errors
Common base with grounded base
  Higher gain and OP1dB
  Requires –ve supply-> huge efficiency drop (large DC current in Re)
  Bias is very sensitive without Re due to exponential relation (ICE vs VBE)
  sensitive to base inductance errors
Common base with base capacitance
  Highest PAE and OP1dB due to capacitance feedback linearization
  Capacitance help stabilization (not shown)
  Stable bias: negligible efficiency due to Rb ; base current is very small
  Gain drops with smaller capacitance
 | Gain*, dB | PAE**, % | Pout**, dBm
CE | 10.7 | 15.4 | 12.0
Grounded CB | 13.1 | 22.4 | 13.5
CB with 600 cap | 9.8 | 29.7 | 15.2
CB with grounded base
CB with base capacitor

## Slide 7: CB viewed as stacked PA cell*
CCB and Cbase creates negative feedback
This negative feedback
  Linearize the amplifier: higher PAE and OP1dB
  Allows voltage swing on the base: with proper design, the output swing increases yielding in higher output power
  Drops the output impedance: improves S22
*A. Ahmed, et al, EUMIC 2018.
PA unit cell/ stack analogy

## Slide 8: PAE invariance*
Assuming lossless matching network
Internal voltages and currents are constant by proper load and base impedances*
(derivation not shown)
The added power per stage is kept constant for the same internal voltages and currents.
*A. Ahmed, et al, EUMIC 2018.
is the magnitude of
is the magnitude of
is the angle of in radians
is the angle of in radians

## Slide 9: Power Amplifier Cell
Common base with base capacitance
Capacitance dropped slightly
  More power and hard compression
  lower output impedance (better S22)
Shunt stub tunes the transistor parasitics
Two cells are combined and driven by a single driver-> better PAE
ADS and HFSS are used for the interconnect and matching circuit simulations
Two combined PA cells

## Slide 10: Driver design
Higher base capacitance:
  more gain
Input ant output are 50W matched
Staggered matching for wider bandwidth
Driver cell

## Slide 11: Combiner Design
Transmission line combiner instead of Wilkinson
Proposed combiner
  Low loss and very compact
  Smaller BW compared to Wilkinson
Wilkinson
  Bulky, high loss and skinny line
  Higher BW
Proposed combiner
Wilkinson combiner

## Slide 12: PA block diagram
Three linearized common base stages
Low loss and compact transmission line combiner
First driver scaled to sustain good PAE
Independent bias for each stage to monitor the current and optimize the PAE
Chip micrograph
1.08mmx0.63mm
Block diagram

## Slide 13: Measurement results
Wide band operation
1dB BW=20GHz
3dB BW=43GHz
VCC1 | VCC2 | VCC3 | VBB1 | VBB2 | VBB3
2.5V | 2.5V | 1.5V | 1.94V | 1.36V | 1.1V
ICC1 | ICC2 | ICC3 | IBB1 | IBB2 | IBB3
121mA | 52mA | 31.8mA | 4.1mA | 1.7mA | 0.95mA
Measured (solid) vs simulated (dotted) S-parameters

## Slide 14: Measurement results
Psat=20.5dBm, and PAE=20.8%
Psat =18.9-20.5dBm over 125-150GHz
VCC1 | VCC2 | VCC3 | VBB1 | VBB2 | VBB3
2.5V | 2.5V | 1.5V | 1.95V | 1.4V | 1.1V
ICC1 | ICC2 | ICC3 | IBB1 | IBB2 | IBB3
130mA | 56mA | 34mA | 5mA | 2mA | 1mA
Measured and simulated Pout, PAE and gain vs input power at 140GHz
Measured and simulated saturated Pout, PAE and gain vs frequency

## Slide 15: State-of-the-art results
Highest PAE for comparable Psat and gain
Ref | Technology | Freq (GHz) | Psat (dBm) | BW3dB GHz++ | Gain at Psat (dB) | Peak PAE % | Size (mm2) | PDC (W) | Psat/Area mW/mm2
‎[2] | 40 nm CMOS | 140 | 14.8 | 17 | 13** | 8.9 | 0.34 | 0.3 | 88.8
‎[4] | 130-nm SiGe HBT | 155-180 | 18.0 | 25 | 23.5** | 4.0 | 0.85 | 1.57* | 74.2
‎[5] | 130-nm SiGe HBT | 112-142 | 17+ | 16 | 29** | 13+ | 1.06 | 0.39* | 47.2
‎[6] | 130-nm SiGe HBT | 131-180 | 14 | 49 | 22** | 5.7 | 0.48 | 0.44* | 52.3
‎[7] | 250-nm InP HBT | 110-150 | 23.2-24.0 | 32.7 | 14-16 | 5.8-7.0 | 1.89 | 3.46 | 134
‎[8] | 250-nm InP HBT | 115-150 | 21-21.8 | 34.8 | 15-17.5 | 8.2-10.5 | 0.75 | 1.54 | 205
This work | 250-nm InP HBT | 125-150 | 18.9-20.5 | 43 | 12.3-15.9 | 14.3-20.8 | 0.69 | 0.52 | 162

## Slide 16: Summary
Demonstration of record PAE at D-band
Teledyne 250nm InP HBT has high fmax and BVCEo
Capacitively linearized common base
  Higher OP1dB, and PAE
  Easier to bias and stabilize
Compact and low loss transmission line network
Driver scaling and bias optimization

## Slide 17: Acknowledgement
This work was supported in part by the Semiconductor Research Corporation and DARPA under the JUMP program.
The authors thank Teledyne Scientific & Imaging for the IC fabrication. The authors would like to thank Zach Griffith for valuable insight and design review.

## Slide 18: References
[1] M. J. W. Rodwell et al., "100-340GHz Systems: Transistors and Applications," 2018 IEDM, San Francisco, CA, 2018.
[2] D. Simic and P. Reynaert, "A 14.8 dBm 20.3 dB Power Amplifier for D-band Applications in 40 nm CMOS," RFIC, Philadelphia, PA, 2018, pp. 232-235.
[3] A. A. Farid, A. Simsek, A. S. H. Ahmed and M. J. W. Rodwell, "A Broadband Direct Conversion Transmitter/Receiver at D-band Using CMOS 22nm FDSOI," RFIC, Boston, MA, USA, 2019, pp. 135-138.
[4] M. Kucharski, H. J. Ng and D. Kissinger, "An 18 dBm 155-180 GHz SiGe Power Amplifier Using a 4-Way T-Junction Combining Network," ESSCIRC 2019, Cracow, Poland, 2019, pp. 333-336.
[5] A. Visweswaran et al., "A 112-142GHz Power Amplifier with Regenerative Reactive Feedback achieving 17dBm peak Psat at 13% PAE," ESSCIRC, Cracow, Poland, 2019, pp. 337-340.
[6] Z. Furqan et al., “A 15.5-dBm 160- GHz high-gain power amplifier in SiGe BiCMOS technology,” IEEE Microwave. Wireless Component. Lett., vol. 27, no. 2, pp. 177–179, Feb. 2017.
[7] Z. Griffith, M. Urteaga and P. Rowell, "A 140-GHz 0.25-W PA and a 55-135 GHz 115-135 mW PA, High-Gain, Broadband Power Amplifier
MMICs in 250-nm InP HBT," IMS, Boston, MA, USA, 2019, pp. 1245- 1248.
[8] Z. Griffith, M. Urteaga and P. Rowell, "A Compact 140-GHz, 150-mW High-Gain Power Amplifier MMIC in 250-nm InP HBT," in IEEE Microwave and Wireless Components Letters, vol. 29, no. 4, pp. 282-284, April 2019.
[9] M. Urteaga, Z. Griffith, M. Seo, J. Hacker, M. Rodwell, “InP HBT Technologies for THz Integrated Circuits”, Proceedings of the IEEE, Vol. 105, No. 6, pp 1051-1067 June 2017.
[10] Cripps, S 'RF Power amplifiers for wireless communications', 2nd Edition, Artech House, 2006, ISBNI-S96-93-018-7, sec 3.7 pp. 61-6S.
[11] H. T. Dabag, et al., "Analysis and Design of Stacked-FET Millimeter-Wave Power Amplifiers," IEEE Trans. MTT, vol. 61, no. 4, pp. 1543-1556, April 2013.
[12] A. S. H. Ahmed, A. A. Farid, M. Urteaga and M. J. W. Rodwell, "204GHz Stacked-Power Amplifiers Designed by a Novel Two-Port Technique," 2018 13th European Microwave Integrated Circuits Conference (EuMIC), Madrid, 2018, pp. 29-32.
[13] A. S. H. Ahmed, A. Simsek, M. Urteaga and M. J. W. Rodwell, "8.6-13.6 mW Series-Connected Power Amplifiers Designed at 325 GHz Using 130 nm InP HBT Technology," 2018 IEEE BiCMOS and Compound Semiconductor Integrated Circuits and Technology Symposium (BCICTS), San Diego, CA, 2018, pp. 164-167.
[14] Z. Griffith, M. Urteaga, P. Rowell, R. Pierson and M. Field, "Multi-finger 250nm InP HBTs for 220GHz mm-wave power," 2012 International Conference on Indium Phosphide and Related Materials, Santa Barbara, CA, 2012, pp. 204-207.
[15] T. B. Reed, Z. Griffith, P. Rowell, M. Field and M. Rodwell, "A 180mW InP HBT Power Amplifier MMIC at 214 GHz," (CSICS), Monterey, CA, 2013, pp. 1-4.
[16] Ahmed S. H. Ahmed, Munkyo Seo, Ali A. Farid, Miguel Urteaga, James F. Buckwalter, and Mark J. W. Rodwell, "A 200mW D-band Power Amplifier with 17.8% PAE in 250-nm InP