## Slide 1: 100-300GHz Wireless
This work was supported in part by the Semiconductor Research Corporation (SRC) and DARPA.
THz workshop, 2020 IEEE WCNC Conference
Mark Rodwell University of California, Santa Barbara
Harish Krishnaswami: Columbia University Debdeep Jena, Alyosha Molnar, Christoph Studer, Huili Xing: Cornell University Dina Katabi: MIT Sundeep Rangan: New York University Amin Arbabian, Srabanti Chowdhury: Stanford Elad Alon, Ali Niknejad, Borivoje Nikolic, Vladimir Stojanovic: University of California, Berkeley Danijela Cabric: University of California, Los Angeles Gabriel Rebeiz: University of California, San Diego Jim Buckwalter, Upamanyu Madhow, Umesh Mishra, Mark Rodwell, Susanne Stemmer: University of California, Santa Barbara Andreas Molisch, Hossein Hashemi: University of Southern California Kenneth O: University of Texas, Dallas

## Slide 2: Wireless above 100GHz
Wireless networks: exploding demand.
Immediate industry response: 5G. 28, 38, 57-71(WiGig), 71-86GHz increased spectrum, extensive beamforming
Next generation (6G ??): above 100GHz.. greatly increased spectrum, massive spatial multiplexing
DOD applications: Imaging/sensing/radar, comms.

## Slide 3: Benefits of Short Wavelengths
Communications: Massive spatial multiplexing, massive # of parallel channels. Also, more spectrum!
Imaging: very fine angular resolution
But: High losses in foul or humid weather. High l2/R2 path losses. ICs: poorer PAs & LNAs. Beams easily blocked.
100-340GHz wireless: terabit capacity, short range, highly intermittent

## Slide 4
140-340 GHz: Applications

## Slide 5: 140GHz massive MIMO hub demo
1 Tb/s spatially-multiplexed 140GHz base station 128 users/face, 4 faces. 21 dBm PAs, F=8dB LNAs 1024 total users @ 1 user/beam, 1,10 Gb/s/beam; 225, 100 m range in 50mm/hr rain with 20dB total margins
Handset: 8 × 8 array (9×9mm)

## Slide 6: 220 GHz, 640 Gb/s MIMO Backhaul
8-element MIMO array 3.1 m baseline. 80Gb/s/subarray→ 640Gb/s total 4 × 4 sub-arrays → 8 degree beamsteering
Key link parameters 500 meters range in 50 mm/hr rain; 23 dB/km 24 dB total margins: packaging loss, obstruction, operating, design, aging PAs: 24mW Pout (per élément) LNAs: 6dB noise figure

## Slide 7: High-resolution imaging radar
Goal: MIMO Imaging Radar Carrier Frequencies: 140, 210GHz

## Slide 8
ICs

## Slide 9: InP HBT to 670 GHz: DARPA TFAST and THz Programs
560 GHz fundamental VCO
340 GHz dynamic frequency divider
620 GHz, 20 dB gain amplifier
M Seo, TSC IMS 2013
also: 670GHz amplifier J. Hacker , TSC IMS 2013 (not shown)
M. Seo, TSC / UCSB
M. Seo, UCSB/TSC IMS 2010
204 GHz static frequency divider (ECL master-slave latch)
Z. Griffith, TSC / UCSB CSIC 2010
300 GHz fundamental PLL
M. Seo, TSC IMS 2011
220 GHz 180 mW power amplifier
T. Reed, UCSB CSICS 2013
600 GHz Integrated Transmitter PLL + Mixer
M. Seo TSC
Integrated 300/350GHz Receivers: LNA/Mixer/VCO
M. Seo TSC
81 GHz 470 mW power amplifier
H-C Park UCSB IMS 2014

## Slide 10: 140GHz CMOS ICs
Hub ICs for MIMO Array Farid (Rodwell) UCSB
8-channel handset array ICs; transmitter and receiver (Rebeiz group), UCSD

## Slide 11: Progress in IC Design: 140GHz InP PAs
110mW power amplifier, 20.8% PAE A. Ahmed, IMS 2020
190mW power amplifier A. Ahmed, submitted.
Also: "A 130-GHz Power Amplifier in a 250-nm InP Process with 32% PAE" Kang Ning (Buckwalter group) 2020 RFIC symposium

## Slide 12
Packages / array modules

## Slide 13: The mm-wave module design problem
How to make the IC electronics fit ? How to avoid catastrophic signal losses ? How to remove the heat ?
Not all systems steer in two planes... ...some steer in only one.
Not all systems steer over 180 degrees... ...some steer a smaller angular range

## Slide 14: Concept: Tile for linear arrays
Terrestrial system: horizontal steering only→ linear array. Space at edges of linear array: room for III-V PAs, LNAs. Alternating-sides feed: 2mm pitch→ room for large GaN PAs. Mounting directly on metal carrier→ heatsinking.

## Slide 15: Concept: module for small angular scanning
Terrestrial system: horizontal + vertical steering → rectangular array. Limited angular steering range (installation)→ spacing >> l/2 Endfire / edge-card geometry: room for III-V PAs, LNAs. Mounting directly on metal carrier→ heatsinking.
If Vivaldi's are replaced with dipoles, element spacing can be reduced to l/2. → potential for wider angular scanning

## Slide 16: 140GHz array module design
-1.4 dB
-0.53 dB
Simulations good: working with Kyocera. June tapeout ?

## Slide 17
Systems

## Slide 18: Beamforming for massive spatial multiplexing
Pure digital beamforming: dynamic range & phase noise requirements: appear to be manageable  Digital back-end processing requirements (die area, DC power): being investigated ?
Analog, hybrid beamforming: Do not appear to significantly improve dynamic range in massive MIMO.

## Slide 19: Progress in System Design
ADCs/DACs: only 3-4 bit ADC/DACs required (Madhow, Studer, Rodwell)
Linearity: Amplifier P1dB need be only 3dB above average power (Madhow).
Phase noise: Requirements same as for SISO (Alon, Madhow, Niknejad, Rodwell)
Efficient digital beamforming: beamspace algorithm=complexity ~N× log(N) (Madhow)
Efficient digital beamforming: low-resolution matrix (Studer)
Efficient channel estimation : fast beamspace algorithm (Studer)
Efficiently addressing true-time-delay problem: "rainbow" FFT algorithm (Madhow)
Array-to-backplane interconnect power: low-power analog baseband 50W links (Rodwell)
Digital beamforming
In progress…
Propagation models and measurements: (Molisch)
Blockage probability, mesh networks, network protocols: (Rangan, Cabric)
MIMO system power analysis: (Rangan, Cabric, Buckwalter)

## Slide 20: Progress: All-Digital Beamformer
mmWave/THz channels are sparse in beamspace domain
Exploiting sparsity can significantly reduce baseband complexity
Challenge: requires fast Fourier transforms (FFTs) at baseband sampling rates
BS antennas | Area | Power
64 | 9mm2 | 2W
128 | 32mm2 | 7W
256 | 122mm2 | 26W
  Synthesis results for 28nm CMOS
Implementation examples
  1 GHz bandwidth
  10b FFTs generated with Spiral
Specialized FFTs (radix-4, higher streaming width, etc.) will further reduce area and power!
Christoph Studer, Cornell

## Slide 21
Transistors

## Slide 22: Progress in mm-Wave Transistors
THz InP HBTs: SOA today: 130nm node, 1.1 THz fmax, 3.5 V breakdown Efficient 100-650GHz power more fmax: more efficient, higher frequencies base regrowth: better contacts→ higher fmax. status: working DC devices; moving to THz
THz InP HBTs: SOA today: 1.5 THz fmax, ~1.1 V breakdown Sensitive 100-650GHz low-noise amplifiers more ft: lower noise, higher frequencies high-K gate dielectric → higher ft. status: process modules
InGaN and GaN HEMTs: High power from 100-340GHz GaN: superior power density at all frequencies UCSB/Mishra: InGaN for increased mobility Cornell/Xing: AlN/GaN/AlN
N-polar GaN: Mishra, UCSB

## Slide 23: Wireless above 100 GHz
Massive capacities large available bandwidths massive spatial multiplexing in base stations and point-point links
Very short range: few 100 meters short wavelength, high atmospheric losses. Easily-blocked beams.
IC Technology All-silicon for short ranges below 250 GHz. III-V LNAs and PAs for longer-range links. Just like cell phones today III-V frequency extenders for 340GHz and beyond
The challenges spatial multiplexing: computational complexity packaging: fitting signal channels in very small areas

## Slide 24
(backup files follow)

## Slide 25: Progress in System Design
ADC resolution: N ADC bits, M antennas, K signals: SNR=6N+1.76+10.log10(M/K) 3 bits, (M/K)=2→ SNR=23 dB. QPSK needs 9.8 dB.
Jammer tolerance: Increase ADC resolution by 1 bit→ Pjammer,max = K.Psignal Maximum jammer power = sum of all user's power.
Phase noise: Phase error sf : SNR= -20.log10(sf)+10.log10(M/K), where MIMO and SISO require similar L(f) .
Beamspace: lower frequencies, many NLOS paths, complicated channel matrix: O(M3) to beamform higher frequencies, few NLOS paths, simpler channel matrix: FFT, O(M.logM) to beamform fewer bits in signal; fewer bits in FFT coefficients.

## Slide 26: The mm-wave module design problem
How to make the IC electronics fit ? 100+ GHz arrays: l0/2 element spacing is very small. Antennas on or above IC → IC channel spacing = antenna spacing → limited IC area to place circuits
How to avoid catastrophic signal distribution losses ? long-range, high-gain arrays: array size can be large. ICs beside array → very long wires between beam former and antenna → potential for very high signal distribution losses
How to remove the heat ? 100+ GHz arrays: element spacing is very small. If antenna spacing = IC channel spacing, then power density is very large

## Slide 27: ComSenTer
Center for Converged Communications & Sensing at THz.
Duration: 5-years; 1/2018-12/2022.
Funding: about $32 million total.
Team: 21 Professors, ~65 Ph.D. students
Sponsors: SRC, DARPA
Focus: wireless systems, 10-15 years out, 100-340GHz

## Slide 28: 100-340 GHz: challenges & solutions
Need mesh networks
Need large arrays
High attenuation in foul or humid weather