## Slide 1
A 200 GHz InP HBT Direct-Conversion
LO-Phase-Shifted Transmitter/Receiver
with 15 dBm Output Power
Munkyo Seo1, Ahmed S. H. Ahmed2,3, Utku Soylu3, Ali Farid3,
Yunsik Na1, and Mark Rodwell3
1Dept of ECE, Sungkyunkwan University, South Korea
2Marki Microwave Inc., USA
3Dept of ECE, University of California, Santa Barbara, USA

## Slide 2: Outline
Motivation
Overview
Transceiver circuit design
Measured results
Summary

## Slide 3: Wireless Communication @ 200 GHz
Motivation
  Large available BW  High data rate (6G)
  Low atmospheric loss @ 200 GHz band
Challenges
  Short wavelength  High path loss
  Low transistor gain  Low efficiency  Low battery life
Proposed 200 GHz transceiver
  InP-HBT  High Pout & high efficiency
  Mixed use of normal & inverted microstrip
  Integrated LO phase shifter  Phased-array
Normal microstrip
1.1 dB/mm @200GHz
Ground holes
PA & LNA
Inverted microstrip
2.5 dB/mm @200GHz
Continuous GND
High-density blocks

## Slide 4: Proposed 200 GHz Transmitter / Receiver
RF
0 o
90 o
25 GHz
TX I-Q mixer
I
Q
x2
x2
x2
Phase
Shifter
PA
LO multiplier
chain
Inverted microstrip
Normal microstrip
RF
LNA
RX I-Q mixer
Inverted microstrip
Normal microstrip
0 o
90 o
25 GHz
x2
x2
x2
Phase
Shifter
LO multiplier
chain
200 GHz direct-conversion TX
200 GHz direct-conversion RX
PA & LNA: Normal microstrip for best PAE and lowest NF
Mixer, LO multiplier, phase shifter: Inverted microstrip for low-inductance ground
Integrated LO phase shifter enables phased-array operation of multiple ICs
I
Q
Size: 2.9 x 0.75 mm2
Size: 2.3 x 0.85 mm2

## Slide 5: 200 GHz PA Design
PA schematic
4-stage common-base w/ Cbase
  Higher efficiency @OP1dB than common-emitter
  Higher efficiency @OP1dB than common-base with no Cbase
Low-loss 2:1 combiner w/ a single λ/4 line & shunt L
Sim: Psat = 17dBm@200GHz, S21 > 20dB, PDC = 450mW
Size: 850 x 550 μm2
PA layout

## Slide 6: 200 GHz LNA Design
3-stage LNA
1-stage
3-stage LNA layout
Size: 350 x 250 μm2
3-stage common-base (CB)
Base cap. adjusted for simultaneous noise & S11 matching
Emitter length scaled for minimum input matching loss
Simulation: S21 = 15dB, 3-dB BW = 35GHz, PDC = 14mW

## Slide 7: LO Frequency Multiplier Design
x2
x2
x2
200 GHz
100 GHz
50 GHz
25 GHz
Cascade of three push-push doublers  x8 LO multiplier
Capacitive emitter degeneration  Operates with wider ranges of Pin
Simulation: Pout > 0dBm for 180-230GHz (BW = 50GHz), PDC = 250mW
Multiplier layout
Size: 580 x 400 μm2
x8 LO multiplier schematic

## Slide 8: 200 GHz LO Phase Shifter
Lange
coupler
I-Q
Vector
Mod.
Balun
Input
0 °
90 °
Output
Sign
control
(I & Q)
Bias
control
(I & Q)
Balun
Balun
Phase shifter schematic
Phase shifter layout
Size: 300 x 400 μm2
Vector-modulator-based phase shifter
Wideband operation by using Lange coupler
Sim: I/Q phase error < 2deg, mag. error < 0.3dB for 170-250GHz, PDC = 100mW

## Slide 9: Transmitter Testing Setup
RF out
200 GHz
TX IC
25.6 GHz (LO)
LO in
Spectrum analyzer
BB in
0 – 20 GHz (BB)
Power meter (PM4)
Harmonic mixer
20 dB coupler
140-220 GHz (WR5) on-wafer testing
Simultaneous freq. & power testing
TX used as a calibration reference

## Slide 10: Measured TX Conversion Gain
Peak conversion gain = 34 dB
3-dB bandwidth > 20 GHz
LO multiplier tuning bandwidth > 30 GHz
Conversion Gain @ fixed fLO
Conversion Gain @ fixed fBB

## Slide 11: Measured TX Output Power
Psat = 16.5 dBm @ fRF = 195 GHz, 15.3 dBm @ fRF = 200 GHz
PDC = 1,250 mW
Pout vs Pin @ fLO=207 GHz (fBB=1 GHz)
Psat vs fRF

## Slide 12: Receiver Testing Setup
RF in
200 GHz
RX IC
BB out
8
Spectrum analyzer
140-220 GHz (WR5) on-wafer testing
Simultaneous freq. & power testing
RX driven by multiplier & variable attenuator
20 dB coupler
Spectrum analyzer
Harmonic mixer
Freq. Multiplier
Var. attenuator
LO
Power meter
20 dB coupler
LO in

## Slide 13: Measured RX Conversion Gain
Peak conversion gain = 25 dB
LO multiplier tuning bandwidth > 25 GHz
Conversion Gain @ fixed fLO
Conversion Gain @ fixed fBB

## Slide 14: Measured RX Power & Noise Figure
Pout vs Pin @ fLO=206 GHz (fBB=1 GHz)
Input P1dB = -24 dBm
Psat = +1 dBm
PDC = 825 mW
Noise Figure
NF = 7.7 – 9.3 dB (200-212 GHz)
Hot/Cold noise source
RX-IC
BB LNA
SA
VDI-WR5.1-NS

## Slide 15: Performance Comparison of Transmitter
This work
This work

## Slide 16: Summary
200 GHz direct-conversion transmitter / receiver in InP HBT
Highest Pout and efficiency, among all integrated TX beyond 200 GHz
Modulated testing is under way

## Slide 17: Acknowledgement
This work was supported by ComSenTer, a JUMP program sponsored by the Semiconductor Research Corporation, by a gift from Samsung corporation and by the Samsung Electronics, under the Grant SRFC-TB1803-06.
The authors thank Teledyne Scientific & Imaging for the IC fabrication.

## Slide 18
Thank you very much!

## Slide 19: References
[1] M. J. W. Rodwell et al., “100-340GHz Systems: Transistors and Applications,” in Proc. IEEE IEDM, 2018, pp. 14.3.1-14.3.4
[2] M. Abbasi et al., “Single-chip 220-GHz active heterodyne receive and transmitter MMICs with on-chip integrated antenna,” IEEE Trans. Microwave Theory and Techniques, vol. 59, no. 2, Feb. 2011.
[3] D. Lopez-Diaz et al., "A subharmonic chipset for gigabit communication around 240 GHz," 2012 IEEE/MTT-S International Microwave Symposium Digest, Montreal, QC, Canada, 2012, pp. 1-3.
[4] Z. Wang, P. Chiang, P. Nazari, C. Wang, Z. Chen and P. Heydari, "A CMOS 210-GHz Fundamental Transceiver with OOK Modulation," in IEEE Journal of Solid-State Circuits, vol. 49, no. 3, pp. 564-580, March 2014.
[5] S. Kang, S. V. Thyagarajan and A. M. Niknejad, "A 240 GHz Fully Integrated Wideband QPSK Transmitter in 65 nm CMOS," in IEEE Journal of Solid-State Circuits, vol. 50, no. 10, pp. 2256-2267, Oct. 2015.
[6] S. Kim et al., "300 GHz Integrated Heterodyne Receiver and Transmitter with On-Chip Fundamental Local Oscillator and Mixers," in IEEE Transactions on Terahertz Science and Technology, vol. 5, no. 1, pp. 92-101, Jan. 2015.
[7] N. Sarmah et al., "A Fully Integrated 240-GHz Direct-Conversion Quadrature Transmitter and Receiver Chipset in SiGe Technology," in IEEE Transactions on Microwave Theory and Techniques, vol. 64, no. 2, pp. 562-574, Feb. 2016.
[8] D. Fritsche, P. Stärke, C. Carta and F. Ellinger, "A Low-Power SiGe BiCMOS 190-GHz Transceiver Chipset with Demonstrated Data Rates up to 50 Gbit/s Using On-Chip Antennas," in IEEE Transactions on Microwave Theory and Techniques, vol. 65, no. 9, pp. 3312-3323, Sept. 2017.
[9] S. Lee et al., "An 80-Gb/s 300-GHz-Band Single-Chip CMOS Transceiver," in IEEE Journal of Solid-State Circuits, vol. 54, no. 12, pp. 3577-3588, Dec. 2019.
[10] P. Rodríguez-Vázquez, J. Grzyb, B. Heinemann and U. R. Pfeiffer, "A 16-QAM 100-Gb/s 1-M Wireless Link with an EVM of 17% at 230 GHz in an SiGe Technology," in IEEE Microwave and Wireless Components Letters, vol. 29, no. 4, pp. 297-299, April 2019.
[11] P. Rodriguez-Vazquez, J. Grzyb, B. Heinemann and U. R. Pfeiffer, "A QPSK 110-Gb/s Polarization-Diversity MIMO Wireless Link With a 220–255 GHz Tunable LO in a SiGe HBT Technology," in IEEE Transactions on Microwave Theory and Techniques, vol. 68, no. 9, pp. 3834-3851, Sept. 2020.
[12] M. H. Eissa, N. Maletic, E. Grass, R. Kraemer, D. Kissinger and A. Malignaggi, "100 Gbps 0.8-m Wireless Link based on Fully Integrated 240 GHz IQ Transmitter and Receiver," 2020 IEEE/MTT-S International Microwave Symposium (IMS), Los Angeles, CA, USA, 2020, pp. 627-630.
[13] H. Hamada et al., "300-GHz-Band 120-Gb/s Wireless Front-End Based on InP-HEMT PAs and Mixers," in IEEE Journal of Solid-State Circuits, vol. 55, no. 9, pp. 2316-2335, Sept. 2020.
[14] A. S. H. Ahmed, M. Seo, A. A. Farid, M. Urteaga, J. F. Buckwalter and M. J. W. Rodwell, "A 140GHz power amplifier with 20.5dBm output power and 20.8% PAE in 250-nm InP HBT technology," 2020 IEEE/MTT-S International Microwave Symposium (IMS), Los Angeles, CA, USA, 2020, pp. 492-495.
[15] A. S. H. Ahmed, U. Soylu, M. Seo, M. Urteaga, J. F. Buckwalter and M. J. W. Rodwell., " A 190-210GHz Power Amplifier with 17.7-18.5dBm Output Power and 6.9-8.5% PAE.," in press, Proc. IMS2021.
[16] A. S. H. Ahmed, M. Seo, A. A. Farid, M. Urteaga, J. F. Buckwalter and M. J. W. Rodwell, "A 200mW D-band Power Amplifier with 17.8% PAE in 250-nm InP HBT Technology," 2020 15th European Microwave Integrated Circuits Conference (EuMIC), Utrecht, Netherlands, 2021, pp. 1-4.
[17] Y. Xing et al., “Propagation measurement system and approach at 140 GHz – Moving to 6G and above 100 GHz,” 2018 IEEE Global Communications Conference.

## Slide 20: Performance Comparison
Ref. | Technology | Integrated TX circuit blocks | Freq. (GHz) | Psat (dBm) | PDC (mW) | Efficiency (%)
[2] | 0.1μm GaAs mHEMT | IF-mixer, LO multiplier (×2), PA, antenna | 220 | -6 | 110 | 0.23
[3] | 50nm GaAs mHEMT | IF-mixer, PA | 240 | 1 | N/A | N/A
[4] | 32nm SOI CMOS | LO VCO, OOK mod, PA, antenna | 210 | 4.6 | 240 | 1.20
[5] | 65nm CMOS | IQ-mixer, tripler | 240 | -0.5 | 220 | 0.41
[6] | 250nm InP-HBT | IF-mixer, LO driver, LO oscillator | 298.1 | -2.3 | 452 | 0.13
[7] | 130nm SiGe | IQ-mixer, LO multiplier (×16), PA | 240 | -4.4 | 1,033 | 0.04
[8] | 130nm SiGe | Mixer, LO driver, antenna | 190 | -6 | 321 | 0.78
[9] | 40nm CMOS | IQ-mixer, LO multiplier (×3) | 265.68 | -1.6 | 890 | 0.08
[10] | 130nm SiGe | IQ-mixer, LO multiplier (×16), PA | 220-255 | 5 | 960 | 0.33
[11] | 130nm SiGe | IQ-mixer, LO multiplier (×16), PA | 225-255 | 7.5 | 9602 | 0.59
[12] | 130nm SiGe | IQ-mixer, LO multiplier (×8), PA | 240 | 124 | 1,237 | 1.28
[13] | 80nm InP-HEMT | IF-mixer, LO driver, PA3 | 290 | 12 | 6,600 | 0.24
This work | 250nm InP-HBT | IQ-mixer, LO multiplier (×8), phase shifter, PA | 195 | 16.5 | 1,250 | 3.57
 |  |  | 200 | 15.3 | 1,250 | 2.71
1PDC not including LO generator at 190 GHz 2PDC for 1-channel I-Q TX+LO 3Individually packaged, not integrated 4Measured from PA breakout