## Slide 1: Packaging challenges in 100-300 GHz wireless.
2021 3DIC - IEEE International 3D Systems Integration Conference, Nov. 15-17, 2021
M. J. W. Rodwell1, Ali A. Farid1, A. S. H. Ahmed1, M. Seo2, U. Soylu1, A. Alizadeh1, N. Hosseinzadeh1
1University of California, Santa Barbara 2Sungkyunkwan University
rodwell@ece.ucsb.edu
Acknowledgement: This work was supported in part by the Semiconductor Research Corporation (SRC) and DARPA.

## Slide 2: Acknowledgements
Also: Kyocera: D. Kim, H. Horikawa, M. Imayoshi. Samsung: G. Xu, N. Sharma, S. Abu-Surra, W. Choi Pi-Radio: A. Dhananjay,

## Slide 3: 100-300GHz Wireless
100-300GHz carriers, massive spatial multiplexing → Terabit hubs and backhaul links, high-resolution imaging radar
Wireless networks: exploding demand.
Immediate industry response: 5G. ~1~40 GHz ("5G?") ~40~100GHz ("5.5G ?") increased spectrum, extensive beamforming
Next generation might be above 100GHz.. (?) greatly increased spectrum, massive spatial multiplexing

## Slide 4: Benefits of Short Wavelengths
Communications: Massive spatial multiplexing, massive # of parallel channels. Also, more spectrum!
Imaging: very fine angular resolution
But: High losses in foul or humid weather. High l2/R2 path losses. ICs: poorer PAs & LNAs. Beams easily blocked.
100-340GHz wireless: terabit capacity, short range, highly intermittent

## Slide 5
Applications

## Slide 6: 140 GHz moderate-MIMO hub
If demo uses 32-element array (four 1×8 modules): 16 users/array. P1dB=21 dBm PAs, F=8 dB LNAs 1,10 Gb/s/beam→ 16, 160 Gb/s total capacity 70, 40 m range in 50 mm/hr rain with 17 dB total margins
Handset: 8 × 8 array (9×9mm)

## Slide 7: 210 GHz, 640 Gb/s MIMO Backhaul
8-element MIMO array 2.1 m baseline. 80Gb/s/subarray→ 640Gb/s total 4 × 4 sub-arrays → 8 degree beamsteering
Key link parameters 500 meters range in 50 mm/hr rain; 23 dB/km 20 dB total margins: packaging loss, obstruction, operating, design, aging PAs: 18dBm =P1dB (per element) LNAs: 6dB noise figure

## Slide 8: 210 GHz FMCW crossed-array imaging car radar
Array: 36×1 transmit, 1×216 receive 36 (v) × 216 (h) image length: 15cm (6 inches), beamwidth: 0.27o, view: 10o (v) ×90o (h). scan: 40Hz Electronics transmit power/element: 50mW receiver noise: 6dB packaging losses: 2dB TX, 2dB RX
Sees: 22cm diameter target (a soccer ball) @ -10dB reflectivity 200m range, with 10dB SNR in heavy fog/rain @ 22dB/km with 4dB operating margins.

## Slide 9
Transistors and ICs

## Slide 10: Transistors for 100-300GHz
CMOS: good power & noise up to ~150GHz. Not much beyond. 65-32nm nodes are best.
InP HBT: record 100-300GHz PAs
SiGe HBT: power better than CMOS, worse than InP HBT
GaN HEMT: record power below 100GHz. Bandwidth improving
InGaAs-channel HEMT: world's best low-noise amplifiers
*results with low PAE at high Psat or low Psat with high PAE are not shown
Results compiled 9/9/2021

## Slide 11: 140GHz Tx/Rx, 22nm SOI CMOS (GlobalFoundries)
1.9 mm
0.76 mm
1.9 mm
0.76 mm
A. Farid UCSB, 2019 RFIC symposium

## Slide 12: Power Amplifiers in 250 nm InP HBT
130GHz, 200mW, 17.8% PAE
140GHz, 20.5dBm, 20.8% PAE
266GHz, 16.8dBm, 4.0% PAE
194GHz, 17.4dBm, 8.5% PAE
Ahmed et al, 2020 IMS, 2020 EuMIC, 2021 IMS, 2021 RFIC
Teledyne 250nm InP HBT technology
Record-setting efficiency for 100-300GHz power amplifiers.

## Slide 13: 210 GHz Transmitter and Receiver ICs
200 GHz direct-conversion TX
200 GHz direct-conversion RX
Size: 2.3 x 0.85 mm2
Size: 2.9 x 0.75 mm2
M. Seo et al, 2021 IMS; Teledyne 250nm InP HBT

## Slide 14: 280GHz transmitter and receiver IC designs
Solyu, Alz, Ahmed, Seo; UCSB/Sungkyunkwan
Teledyne 250nm InP HBT technology
Receiver
Transmitter
simulations: 11dB noise figure, 40GHz bandwidth
simulations: 17dB saturated output power.
Application: point-point MIMO backhaul links

## Slide 15
140 GHz Array Modules

## Slide 16: The mm-wave module design problem
How to make the IC electronics fit ? How to avoid catastrophic signal losses ? How to remove the heat ?
Not all systems steer in two planes... ...some steer in only one.
Not all systems steer over 180 degrees... ...some steer a smaller angular range

## Slide 17: Do we need 2D arrays ? 1D steering might be fine.
1/sin2f sidelobes provide strong signals to tall buildings.
Providing sidelobes reduces broadside gain by less than 3dB.
→ Don't need 2D arrays to serve tall buildings

## Slide 18: 2D vs. 1D: user spatial distribution
design 1: 2D array
design 2: 1D array
uniform horizontal & vertical user distributions
uniform horizontal, nonuniform vertical

✘


Spatial distribution of users, and of scattering objects, guides choice of array geometry.

## Slide 19: 1D or 2D subarray for backhaul ?
Should we use 4x4 array, 1x16, or 16x1 array ? All provide same system link budget, same # RF channels, same angular scanning range.
Spatial distribution of users, and of scattering objects, guides choice of array geometry.

## Slide 20: 140GHz hub: packaging challenges
IC-package interconnects Difficult at > 100 GHz
Removing heat Thermal vias are marginal
Interconnect density Dense wiring for DC, LO, IF, control. Hard to fit these all in.
Economies of scale Advanced packaging standards require sophisticated tools High-volume orders only Hard for small-volume orders (research, universities) Packaging industry is moving offshore

## Slide 21: 100-300GHz IC-package connections
type | Frequency | technology | cost | heatsinking
micromachined waveguide interface | 1000 GHz | Research. Cheap one day ? | high ✘ | good
ribbon, mesh bond | 200 GHz | Handcrafted. | high ✘ | good
patch antennas on superstrate | 1000 GHz | Straightforward | low | good
Cu stud flip-chip | >200 GHz | Industry standard | low | ok, marginal for PA ✘
hot vias | 200 GHz | Development | low ? | good
(ball) wirebonds | 100 GHz ✘ | Industry standard | low | good
Deal, IEEE Trans THz, Sept 2011
G. Rebeiz

## Slide 22: 140GHz hub: ICs & Antennas
110mW InP Power Amplifier 20.8% PAE
190mW InP Power Amplifier 16.7% PAE
CMOS Transmitter IC 22nm SOI CMOS.
Receiver IC 22nm SOI CMOS.
LTCC Array module
1 cm
Teledyne InP HBT
GlobalFoundries 22nm SOI CMOS
Kyocera
Farid, Ahmed, Rodwell, UCSB; Flynn, Dunn, Niknejad, Nikolic, BWRC; Rebeiz, UCSD

## Slide 23: 135GHz 8-channel MIMO hub array tile modules
Receiver: A. Farid et. al, 2021 IEEE BCICTS Symposium
Transmitter: Results to be submitted

## Slide 24
210 GHz and 280 GHz Array Modules

## Slide 25: 210 GHz MIMO backhaul demo
8-element MIMO array 3.1 m baseline for 500m link. 80Gb/s/subarray→ 640Gb/s total 4 × 4 sub-arrays → 8 degree beamsteering
Key link parameters 500 meters range in 50 mm/hr rain; 23 dB/km 20 dB total margins: packaging loss, obstruction, operating, design, aging PAs: 63mW =P1dB (per element) LNAs: 6dB noise figure

## Slide 26: 210GHz Module: Single-Channel Backup Plan

## Slide 27: 210GHz Series Feed Antenna on 50 mm Fused Silica

## Slide 28
Advanced Packages

## Slide 29: The mm-wave module design problem
How to make the IC electronics fit ? How to avoid catastrophic signal losses ? How to remove the heat ?
Not all systems steer in two planes... ...some steer in only one.
Not all systems steer over 180 degrees... ...some steer a smaller angular range

## Slide 30: Materials for 100-300GHz Packages

## Slide 31: Packages for medium-to-high-power 1D arrays
PA heatsinking: good-high thermal conductivity under ICs
Even 1D arrays are dense: IF, power, control, LO/N lines must run under IC need OK line losses @ DC~30GHz → moderate dielectric constant, high thermal K. ceramic AlN or SiC ? (~200W/K/M)
Need high-quality 100-300GHz antennas one thin and low-er insulator plane required. fused silica or similar. for high-performance antennas for 100-300GHz routing, if needed

## Slide 32: Ceramic AlN and SiC
Crystalline AlN and SiC are expensive. Ok for high-performance DOD packages need cheaper package material for industry, consumers
Ceramic AlN and SiC can be substantially less expensive lower thermal conductivity can be formed into thick layers ceramic AlN apparently has Kth~100W/K/m ceramic SiC apparently has Kth~180W/K/m excellent for many packages
https://www.ortechceramics.com/products/uncategorized/aluminum-nitride-substrate/
http://www.surmet.com/technology/aln/index.php
https://precision-ceramics.com/materials/aluminum-nitride/
https://www.accuratus.com/alumni.html
https://global.kyocera.com/prdct/fc/list/material/silicon_carbide/index.html?gclid=CjwKCAjwvuGJBhB1EiwACU1AiftisyIcz-7Zw1pUJ2FXYrgWSHwlq1sCKNcSA6dtuBwhc6aw_cmEzBoC54EQAvD_BwE
https://global.kyocera.com/prdct/fc/product/category/life/life011.html

## Slide 33: The 100-300GHz 2D Array Challenge
f | 100 | 150 | 200 | 250 | 300 | GHz
l | 3 | 2 | 1.5 | 1.2 | 1 | mm
l/2 | 1.5 | 1 | 0.75 | 0.6 | 0.5 | mm
0.6l | 1.8 | 1.2 | 0.9 | 0.72 | 0.6 | mm
System architecture: Single-beam: simpler RF front-end, simpler baseband MIMO: complex digital baseband, flexible, many beams
Arrays can be made from either tiles or trays
Arrays must be vast: 100-1,000-10,000 elements
Arrays must be dense: packaging challenges Many DC/IF/LO lines, plus antenna interface. Fitting IC functions into available area. Removing the heat.

## Slide 34: The 100-300GHz 2D Arrays: tiles vs. trays
Tiles: thinner, cheaper, lighter less space to fit the electronics: ~0.6l × 0.6l more difficult to remove the heat
Trays (Slats): thicker, more expensive, heavier more space to fit the electronics: ~ L × 0.6l easier to remove the heat

## Slide 35: A simple 200GHz, 0.6l×0.6l array can just fit
24-element array 4.5mm × 4.5mm
Seo et al, 2021 IMS

## Slide 36: Packages for medium-to-high-power 2D arrays
PA heatsinking: good-high thermal conductivity material under ICs
2D arrays are very dense: IF, power, control, LO reference lines must run under IC need OK line losses @ DC~30GHz → moderate dielectric constant, high thermal K. ceramic AlN or SiC (~200W/K/M) possibly LTCC; need better thermal vias, better density.
Need high-quality 100-300GHz antennas above ICs. need thin low-er insulator plane above IC. fused silica superstrate.

## Slide 37: 100-300GHz array frequency scaling
(Worst-case atmospheric loss: ~constant over 50-300GHz)
Proposed scaling law | change
carrier frequency | increase 2:1
aperture area | keep constant
total transmit power | keep constant
Implication | change
capacity (# beams·bit rate per beam) | increases 4:1
number elements | increases 4:1
RF power per cm2 aperture area | stays constant
RF power per element | decreases 4:1
IC area/element (tiled array) | decreases 4:1
IC area/element (trayed array) | decreases 2:1
IC power/area (tiled array) | stays constant
IC power/area (trayed array) | decreases 2:1

## Slide 38: 2D arrays with ICs *beside* antennas
Concept: N × N 2D array array RF ICs placed at sides 50W striplines between ICs and antennas
Interconnect losses are acceptable line lengths are <Nl/4: low loss
Interconnect density limits array size: Assume: 4-layer LCP interposer (75 mm layers, er~3.3), 50W striplines are 75 mm wide minimal line coupling: 150 mm line spacings → 4 interconnects in l/2 pitch of 140GHz array. → 8×8 maximum array tile size at 140GHz → 16×16 maximum array tile size at 75GHz
IC channel density limits array size: l/2 antenna pitch, N × N antenna array fed from both sides → IC channel pitch = l/N. Assume 250 mm channel pitch: → 8×8 maximum array tile size at 140GHz → 16×16 maximum array tile size at 75GHz

## Slide 39
Packaging for 100-300GHz Wireless

## Slide 40: Packaging for 100-300GHz wireless
Overall Challenges: 100-300GHz antenna-IC connections removing heat. Interconnect density Supply chain (domestic, R&D small-volume)
Established technologies: effective for 1D arrays and smaller 2D arrays. Low-er (LCP, organic, LTCC) interposers: good antennas Cu stud flip-chip bonding: good connections thermal challenges: thermal via performance and density
Advanced technologies High-power 1D arrays: package laminates with both low-er and high-Kth layers Medium-power 2D tiled arrays: low-er antenna superstrate, high-Kth interconnect substrate Medium-power 2D trayed arrays: assembly cost, high-Kth trays

## Slide 41
(backup files follow)