## Slide 1: 100-300GHz Wireless: ICs, Arrays, and Systems
2021 IEEE BiCMOS and Compound Semiconductor Integrated Circuits and Technology Symposium (BCICTS): December 6-9
M. J. W. Rodwell1, Ali A. Farid1, A. S. H. Ahmed1, M. Seo2, U. Soylu1, A. Alizadeh1, N. Hosseinzadeh1
1University of California, Santa Barbara 2Sungkyunkwan University
rodwell@ece.ucsb.edu
Acknowledgement: This work was supported in part by the Semiconductor Research Corporation (SRC) and DARPA.

## Slide 2: Acknowledgements
Also: Kyocera: D. Kim, H. Horikawa, M. Imayoshi. Samsung: G. Xu, N. Sharma, S. Abu-Surra, W. Choi Pi-Radio: A. Dhananjay,

## Slide 3: 100-300GHz Wireless
100-300GHz carriers, massive spatial multiplexing → Terabit hubs and backhaul links, high-resolution imaging radar
Wireless networks: exploding demand.
Immediate industry response: 5G. ~1~40 GHz ("5G?") ~40~100GHz ("5.5G ?") increased spectrum, extensive beamforming
Next generation might be above 100GHz.. (?) greatly increased spectrum, massive spatial multiplexing

## Slide 4: Benefits of Short Wavelengths
Communications: Massive spatial multiplexing, massive # of parallel channels. Also, more spectrum!
Imaging: very fine angular resolution
But: High losses in foul or humid weather. High l2/R2 path losses. ICs: poorer PAs & LNAs. Beams easily blocked.
100-340GHz wireless: terabit capacity, short range, highly intermittent

## Slide 5
Applications

## Slide 6: 140GHz moderate-MIMO hub
If demo uses 32-element array (four 1×8 modules): 16 users/array. P1dB=21 dBm PAs, F=8dB LNAs 1,10 Gb/s/beam→ 16, 160 Gb/s total capacity 70, 40 m range in 50mm/hr rain with 17dB total margins
Handset: 8 × 8 array (9×9mm)

## Slide 7: 70 GHz spatially multiplexed base station
If we use instead a 70GHz carrier, the range increases to 70 meters (vs. 40 meters) but the handset becomes 16mm×16mm (vs. 8mm×8mm), and the hub array becomes 19mm×612mm (vs. 10mm×328mm)
Or, use a 4×4 (8mm×8mm) handset array, and the range becomes ..about 40 meters.
Same handset area (more handset elements)→ same link budget Easier to obtain license for 140±2.5GHz than 70±2.5GHz

## Slide 8: 210 GHz, 640 Gb/s MIMO Backhaul
8-element MIMO array 2.1 m baseline. 80Gb/s/subarray→ 640Gb/s total 4 × 4 sub-arrays → 8 degree beamsteering
Key link parameters 500 meters range in 50 mm/hr rain; 23 dB/km 20 dB total margins: packaging loss, obstruction, operating, design, aging PAs: 18dBm =P1dB (per element) LNAs: 6dB noise figure

## Slide 9: 75 GHz, 640 Gb/s MIMO backhaul (16QAM)
Why not use a lower-frequency carrier, e.g. 75 GHz ? Must use at least 16QAM, given 80Gb/s/channel…
Similar RF power output, physically larger
8-element 640Gb/s linear array:
requires 16dBm transmit power/element (Pout)
requires 3.5m linear array

## Slide 10
Systems

## Slide 11: System Design
ADCs/DACs1: QPSK needs only 3-4 bit ADC/DACs N ADC bits, M antennas, K signals: SNR=6N+1.76+10.log10(M/K) 3 bits, (M/K)=2→ SNR=23 dB. QPSK needs 9.8 dB.
Linearity1: Amplifier P1dB need be only 4 dB above average power
Phase noise2,3: Requirements same as for SISO
Efficient digital beamforming4,5: beamspace algorithm=complexity ~N× log(N)
Efficient VLSI digital beamformer implementation6: low-resolution matrix
Efficiently beamforming in broadband arrays7: combined spatial & temporal FFTs.
1) M. Abdelghany et al, IEEE Trans. Wireless Comm, Sept. 2021, doi: 10.1109/TWC.2021.3069378. 2) M. E. Rasekh et al, IEEE Trans. Wireless Comm, Oct. 2021, doi: 10.1109/TWC.2021.3074911. 3) A. Puglielli et al, 2016 IEEE ICC, doi: 10.1109/ICC.2016.7511631. 4) M. Abdelghany, et. al, , 2019 IEEE SPAWC: doi: 10.1109/SPAWC.2019.8815585 5) S. H. Mirfarshbafan et al, IEEE Trans CAS 1, 2020, doi: 10.1109/TCSI.2020.3023023 6) O Castañeda Fernández et. al, 2021 ESSCIRC 7) M. Abdelghany et al 2019 IEEE GLOBECOM doi: 10.1109/GLOBECOM38437.2019.9013233.

## Slide 12
Transistors

## Slide 13: Transistors for 100-300GHz
CMOS: good power & noise up to ~150GHz. Not much beyond. 65-32nm nodes are best.
InP HBT: record 100-300GHz PAs
SiGe HBT: power better than CMOS, worse than InP HBT
GaN HEMT: record power below 100GHz. Bandwidth improving
InGaAs-channel HEMT: world's best low-noise amplifiers
*results with low PAE at high Psat or low Psat with high PAE are not shown
Results compiled 9/9/2021

## Slide 14: InP Transistors and ICs
InP HEMTs: 1.5THz fmax, 1.0THz amplifiers
W. Deal et al, 2016 IEDM (Northrop-Grumman)
130nm InP HBTs: 1.1THz fmax, 3.5V. 670 GHz amplifiers
M. Urteaga, et al, IEEE Proceedings June 2017 (Teledyne)
250nm InP HBTs: 650GHz fmax, 4.5V.
Z. Griffith et al, 2007 IPRM conference (UCSB)
M. Urteaga, et al, IEEE Proceedings June 2017 (Teledyne)

## Slide 15
Power Amplifiers

## Slide 16: 100-300GHz Power combining: what is best ?
Corporate T-line
Direct series-connected M. Shifrin: 1992 IEEE mWave/mmWave Monolithic Circuits Symp. (Raytheon)
Cascaded combining A. Ahmed 2018 EuMIC, 2021 RFIC (UCSB)
Distributed Active Transformer I. Aoki, IEEE Trans MTT, Jan. 2002 (CalTech)
Sub-l/4-coupler series-connected H. Park, et al, IEEE JSSC, Oct. 2014 (UCSB)

## Slide 17: Recent high-efficiency 100-300GHz PAs
130GHz, 200mW, 17.8% PAE
140GHz, 20.5dBm, 20.8% PAE
266GHz, 16.8dBm, 4.0% PAE
194GHz, 17.4dBm, 8.5% PAE
Ahmed et al, 2020 IMS, 2020 EuMIC, 2021 IMS, 2021 RFIC
Teledyne 250nm InP HBT technology
Mixture of corporate and cascade power-combining.

## Slide 18
140 GHz Array Modules

## Slide 19: The mm-wave module design problem
How to make the IC electronics fit ? How to avoid catastrophic signal losses ? How to remove the heat ?
Not all systems steer in two planes... ...some steer in only one.
Not all systems steer over 180 degrees... ...some steer a smaller angular range

## Slide 20: Do we need 2D arrays ? 1D steering might be fine.
1/sin2f sidelobes provide strong signals to tall buildings.
Providing sidelobes reduces broadside gain by less than 3dB.
→ Don't need 2D arrays to serve tall buildings

## Slide 21: 2D vs. 1D: user spatial distribution
design 1: 2D array
design 2: 1D array
uniform horizontal & vertical user distributions
uniform horizontal, nonuniform vertical

✘


Spatial distribution of users, and of scattering objects, guides choice of array geometry.

## Slide 22: 140GHz hub: packaging challenges
IC-package interconnects Difficult at > 100 GHz
Removing heat Thermal vias are marginal
Interconnect density Dense wiring for DC, LO, IF, control. Hard to fit these all in.
Economies of scale Advanced packaging standards require sophisticated tools High-volume orders only Hard for small-volume orders (research, universities) Packaging industry is moving offshore

## Slide 23: 100-300GHz IC-package connections
type | Frequency | technology | cost | heatsinking
micromachined waveguide interface | 1000 GHz | Research. Cheap one day ? | high ✘ | good
ribbon, mesh bond | 200 GHz | Handcrafted. | high ✘ | good
patch antennas on superstrate | 1000 GHz | Straightforward | low | good
Cu stud flip-chip | >200 GHz | Industry standard | low | ok, marginal for PA ✘
hot vias | 200 GHz | Development | low ? | good
(ball) wirebonds | 100 GHz ✘ | Industry standard | low | good
Deal, IEEE Trans THz, Sept 2011
G. Rebeiz

## Slide 24: 140GHz hub: ICs & Antennas
110mW InP Power Amplifier 20.8% PAE
190mW InP Power Amplifier 16.7% PAE
CMOS Transmitter IC 22nm SOI CMOS.
Receiver IC 22nm SOI CMOS.
LTCC Array module
1 cm
Teledyne InP HBT
GlobalFoundries 22nm SOI CMOS
Kyocera
Farid, Ahmed, Rodwell, UCSB; Flynn, Dunn, Niknejad, Nikolic, BWRC; Rebeiz, UCSD

## Slide 25: 135GHz 8-channel MIMO hub array tile modules
Receiver: A. Farid et. al, 2021 IEEE BCICTS Symposium
Transmitter: Results to be submitted

## Slide 26
210 GHz and 280 GHz Array Modules

## Slide 27: 210 GHz MIMO backhaul demo
8-element MIMO array 3.1 m baseline for 500m link. 80Gb/s/subarray→ 640Gb/s total 4 × 4 sub-arrays → 8 degree beamsteering
Key link parameters 500 meters range in 50 mm/hr rain; 23 dB/km 20 dB total margins: packaging loss, obstruction, operating, design, aging PAs: 63mW =P1dB (per element) LNAs: 6dB noise figure

## Slide 28: 210 GHz Transmitter and Receiver ICs
200 GHz direct-conversion TX
200 GHz direct-conversion RX
Size: 2.3 x 0.85 mm2
Size: 2.9 x 0.75 mm2
M. Seo et al, 2021 IMS; Teledyne 250nm InP HBT

## Slide 29: 280GHz transmitter and receiver IC designs
Solyu, Alz, Ahmed, Seo; UCSB/Sungkyunkwan
Teledyne 250nm InP HBT technology
Receiver
Transmitter
simulations: 11dB noise figure, 40GHz bandwidth
simulations: 17dB saturated output power.
Application: point-point MIMO backhaul links

## Slide 30
100-300GHz Wireless

## Slide 31: Wireless above 100 GHz
Massive capacities large available bandwidths massive spatial multiplexing in base stations and point-point links
Very short range: few 100 meters short wavelength, high atmospheric losses. Easily-blocked beams.
IC Technology All-silicon for short ranges below 200 GHz. SiGe or III-V LNAs and PAs for longer-range links. Just like cell phones today III-V frequency extenders for 340GHz and beyond
The challenges computational complexity packaging: fitting signal channels in very small areas mesh networking to accommodate beam blockage driving the technologies to low cost

## Slide 32
(backup files follow)