## Slide 1: Engineering the Future: Toward Self-Organizing, Self-Improving, Self-Healing, and Self-Sustaining Systems
Behrooz Parhami
Dept. Electrical & Computer Eng.
University of California, Santa Barbara
Notes: Abstract: Information and computer systems already have some of the four attributes named in the title of this talk, and they are moving in the direction of greater agility, robustness, and independence. The four notions of self-organization, self-improvement, self-healing, and self-sustenance are not independent. Rather, the four attributes are overlapping in terms of techniques used to design, implement, and assess them. For example, reconfiguration strategies are applicable to self-organization, self-improvement, and self-recovery, while automatic learning is mandatory for both self-organization and self-improvement. This talk presents a number of relationships between these ideas, the nomenclature for talking about them in the context of various types of systems, and examples to demonstrate how they are used in human-made and natural systems.
The annotated slides for this talk, in both PowerPoint and PDF formats, are made available via B. Parhami’s Publications Web page. See item [283] in:
http://www.ece.ucsb.edu/~parhami/publications.htm

## Slide 2: مهندسی‌ در آینده: به سویِ سیستمها یِ خود سازمانده، خود بهساز، خود ترمیم، و خود نگهدار
بهروز پرهامی
دانشکده ی مهندسی‌ برق و کامپیوتر
دانشگاهِ کالیفرنیا در سانتا باربارا
Notes: The talk was delivered in Persian, but the slides are in English. This Persian title slide is meant to establish the Persian equivalents of the four key notions discussed in the talk.

## Slide 3: Today, I Will Do Some Forecasting
Nobel Laureate Physicist Niels Bohr said: “Prediction is very difficult, especially if it’s about the future.” [Paraphrased by Yogi Berra in his famous version]
Anon. quotes about the perils of forecasting: “Forecasting is the art of saying what will happen, and then explaining why it didn’t.” “There are two kinds of forecasts: lucky and wrong.” “A good forecaster is not smarter than everyone else; he merely has his ignorance better organized.”
Henri Poincare was more positive on prediction: “It is far better to foresee even without certainty than not to foresee at all.”
B. Parhami
Engineering the Future
Slide # 03
Notes: Forecasting is notoriously difficult in computer science and engineering. The historical record is rife with predictions that sound laughable now. Examples include Ken Olson’s 1977 assertion that no one would ever want a computer at home and Bill Gates’ 1981 forecast that 640 KB of memory should be enough for any personal computer. Similar gaffes have been made for other technologies, a noteworthy case being Thomas Edison’s pronouncement that working on alternating current is a waste of time, because no one would use it.

## Slide 4: Engineering the Future: System Attributes Toward Self-Organizing, Self-Improving, Self-Healing, and Self-Sustaining Systems
B. Parhami
Engineering the Future
Slide # 04
Survival
Agility
Agency
Self-Healing
Self-Sustaining
Self-Organizing
Self-Improving
Managed
Autonomous
Notes: Information and computer systems can be classified according to three orthogonal attributes. This talk focuses on the agility and survival dimensions, but we should have the agency dimension in the back of our minds, given that a super-agile and highly survivable system may not be stoppable by simply pulling its plug.

## Slide 5: Engineering the Future: Human Analogies Toward Self-Organizing, Self-Improving, Self-Healing, and Self-Sustaining Systems
Self-Organizing: Humans do it by evolution and adaptation; systems can use (re)configuration
Self-Improving: Done through learning and practicing in both humans and machines
Self-Healing: Humans have immune systems and cell regeneration mechanisms; systems need means for fault tolerance and built-in test/repair
Self-Sustaining: Humans need shelter, food, water, air; systems need protection and energy
B. Parhami
Engineering the Future
Slide # 05
Notes: Persian equivalents of the four key attributes and other notions discussed in this talk:
Self-organizing = khod-saazemaan-deh;
Self-improving = khod-behsaaz;
Self-healing = khod-tarmim;
Self-sustaining = khod-negahdaar;
Reconfiguration = baaz-peikar-bandi;

## Slide 6: The Four Notions Are Not Independent
Self-Organizing
Self-Improving
Self-Healing
Self-Sustaining
Learning
Self-Monitoring;
Redundancy
B. Parhami
Engineering the Future
Slide # 06
Energy
Scavenging
Energy
Frugality
Reconfiguration
Notes: The four key attributes are overlapping in terms of techniques used to design, implement, and assess them. For example, reconfiguration strategies are applicable to self-organization, self-improvement, and self-recovery, while automatic learning is mandatory for both self-organization and self-improvement.

## Slide 7: Self-Organization: Introduction
Reconfiguration (self-directed)
  There is an underlying structure (parts and links)
  A subset is configured for the desired functionality
Self-Assembly
  Parts are specially designed to fit with each other
  Perturbation is used to move the parts into position
Evolutionary design
  System structure evolves through adaptation
  Designs have been obtained that are highly optimal
B. Parhami
Engineering the Future
Slide # 07
Notes: Note 1: 3D printing is replacing self-assembly in some domains.
Note 2: Ideas on self-organization are presented in an International Conference on Self-Adaptive and Self-Organizing (SASO) Systems. The 2014 conference will be held on September 8-12, 2014 and is co-located with the Cloud and Autonomic Computing Conference.

## Slide 8: Self-Organization: Reconfiguration
Redundancy
Embedded switches
Malfunction detection
New working configuration
Switch fault tolerance
B. Parhami
Engineering the Future
Slide # 08
Spare
row
Spare
column
Notes: For details and references, see:
B. Parhami, Introduction to Parallel Processing: Algorithms and Architectures, Plenum, 1999, pp. 396-399.
Here is an animated GIF showing one shape morphing into another:
https://groups.csail.mit.edu/drl/wiki/images/f/f6/dogcouch-xsim.gif

## Slide 9: Self-Organization: Self-Assembly
Parts are made so that they self-assemble in the appropriate way when prodded or shaken
B. Parhami
Engineering the Future
Slide # 09
Notes: The 1-minute video embedded in this slide as an example of self-assembly can be found at:
https://www.youtube.com/watch?v=DUa5g5JZR5s

## Slide 10: Self-Organization: Evolutionary Design
Candidate circuits, obtained by randomly varying an already working model, are tested
  Simulation
  3D printing
  FPGAs
  FP Analog Arrays
  FP Transistor Arrays
Evolutionary changes done along many branches
Circuits converge to the desired behavior over many generations
B. Parhami
Engineering the Future
Slide # 010
Notes: Evolutionary design is particularly useful for analog circuits, as we have fairly good methodologies in place for designing digital circuits from behavioral specifications. In analog circuit design, an experienced designer places and connects various components according to their known functionalities. Sometimes, a desired behavior occurs from unusual combination or placement of circuit elements that cannot be explained with existing theories. Evolutionary design is good at discovering these unusual, and often highly efficient, combinations.

## Slide 11: Example 1: The Human Brain
B. Parhami
Engineering the Future
Slide # 011
The human brain has a very inelegant design
Reptilian brain
Limbic system
Neocortex
Ad-hoc additions over eons
Functional redundancy
Layered improvement
Electrochemical signals
Slow signaling
Yet, functionally effective!
Notes: A good, nontechnical overview of the human brain’s hardware can be found in:
Linden, David J., The Accidental Mind: How Brain Evolution Has Given Us Love, Memory, Dreams, and God, Harvard Univ. Press, 2007.

## Slide 12: Self-Improvement: Introduction
B. Parhami
Engineering the Future
Slide # 12
Learning
  Supervised: feedback for good/bad outcomes
  Unsupervised: survival as guide (well-being function)
Energy frugality
  Mobile devices—battery life, energy capacity (Wh/g)
  Supercomputers—energy and cooling costs
Building expertise and “common sense”
  Easier now that nearly all knowledge is on-line
  Turing test is already passed or will be soon
Notes: Some notions of self-improvement (~ self-optimization) are discussed under autonomic computing, which is a broad field of R&D with an annual conference; the 2014 International Conference on Cloud and Autonomic Computing will be held on September 8-12, 2014.

## Slide 13: Self-Improvement: Learning
Specialized knowledge
Neural networks
Reinforcement and training
Word games/puzzles (Watson)
General Q/A system
Turing test (has it been passed already?)
B. Parhami
Engineering the Future
Slide # 013
Notes: Research in machine learning has a long history and is very broad. MIT, Stanford, and other leading universities offer free material (including lecture notes) for an introductory course on the topic that introduces basic techniques in machine learning, beginning with classification and linear regression and concluding with more advanced tools such as boosting, support vector machines, hidden Markov models, and Bayesian networks.

## Slide 14: Example 2: Passing the Turing Test
B. Parhami
Engineering the Future
Slide # 014
A computer is “intelligent” if it can carry out a conversation with a human in a way that the human cannot tell whether she is conversing with a computer or with another human
Conversation must be unrestricted
Fooling a human isn’t hard (in the short term)
A few weeks ago, there was a claim of success
Others have doubted that claim
Turing test will be passed by 2020, for sure
Notes: In June 2014, there were reports of a computer system pretending to be a 13-year-old Ukrainian boy (conversing in English) having passed the Turing Test.
http://www.theguardian.com/technology/2014/jun/08/super-computer-simulates-13-year-old-boy-passes-turing-test

## Slide 15: Self-Healing: Introduction
Redundancy
  More parts and functionality than needed
  Of no use if we cannot detect failures promptly
Self-Monitoring
  Design for concurrent or on-line testing
  Watchdogs, multi-channel operation, coding
Dependability attributes
  Reliability, availability, performability, safety
  Experimental verification of high reliability
B. Parhami
Engineering the Future
Slide # 015
Notes: This is one of B. Parhami’s research foci, and so a bit more detail is presented in the slides that follow. A couple of useful references follow. There is also an annual international conference on Dependable Systems and Networks, which is a primary forum for research results on self-healing systems. Also look for a 2014 special issue of Proceedings of the IEEE on “Trustworthy Hardware.”
Schneider, C., A. Barker, and S. Dobson, “A Survey of Self-Healing Systems Frameworks,” Software Practice and Experience, published on-line 20 Jan. 2014.
Ghosh, D., R. Sharman, H. R. Rao, and S. Upadhyaya, “Self-Healing Systems—Survey and Synthesis,” Decision Support Systems, Vol. 42, pp. 2164-2185, 2007.

## Slide 16: Self-Healing: Static Redundancy
Valves that malfunction in two modes
Redundancy for control
No single malfunction takes away our control
Bridge circuit R = r
Resistors may open/short
  One short: R = r/2
  One open: R = 3r/2
B. Parhami
Engineering the Future
Slide # 016
Stuck open
Stuck shut
r
r
r
r
Notes: Example of redundancy (akin to safety factor in structural engineering) used to overcome the effects of malfunctioning components. These and other techniques are discussed in detail in B. Parhami’s book (under development) on dependable computing, available at:
http://www.ece.ucsb.edu/~parhami/text_dep_comp.htm

## Slide 17: Self-Healing: Dynamic Redundancy
Voting as static redundancy
Standby: hot or cold
Embedded monitors/switches
Deriving a new configuration
Switch fault tolerance
B. Parhami
Engineering the Future
Slide # 017
C
1
Comparator
2
Error
C
1
Comparators
2
Error
C
1
2
Error
S
Switch
V
S
2
3
1
4
Switch-voting unit
Spare
V
2
3
1
Voting unit
Notes: Voting is an example of static redundancy, where additional circuits are built in and “mask” the effect of malfunctions. One drawback of static redundancy is an increase in power requirement. Dynamic redundancy can reduce both the hardware investment and the energy cost for the same reliability level, but it may lead to safety compromises due to imperfection in malfunction detection and recovery.

## Slide 18: Example 3: N-Modular Reduncancy
B. Parhami
Engineering the Future
Slide # 018
Condition on the module reliability:
R = Rm [1 + (1 – Rm)(2Rm – 1)]
(1 – Rm)(2Rm – 1) > 0  Rm > 1/2
V
2
3
1
Voting unit
R
Rm
1.0
0.0
1.0
0.5
0.0
0.5
TMR better
Simplex better
RIFTMR/Simplex = (1 – Rm)/(1 – R)
= 1/[1 – Rm(2Rm – 1)]
R = 3Rm2 – 2Rm3 > Rm
?
TMR:
lt
R
0
0.5
1.0
ln 2
0.0
TMR
Simplex
MTTF: TMR 5/(6l)
Simplex 1/l
1
5
6
TMR
Notes: Triple-modular redundancy (TMR) will be better than a simplex system (no redundancy) only if modules are fairly reliable and the voting circuit is either perfect or much more reliable than the circuits it monitors.
MTTF = Mean time to failure
RIF – Reliability improvement factor

## Slide 19: Self-Sustenance: Introduction
Protection
  Accidental or random influences
  Malicious actions (attacks)
Adaptation
  Directing resources to more critical functions
  Changing accuracy and frequency
Energy scavenging
  Extracting energy from light, heat, vibration, etc.
  Bio-inspired and bio-augmented designs
B. Parhami
Engineering the Future
Slide # 019
Notes: Regarding system sustenance with respect to energy, look for a forthcoming special issue of Proceedings of the IEEE on “Energy Harvesting/Scavenging”

## Slide 20: Example 4: Mars Rover
B. Parhami
Engineering the Future
Slide # 020
Several NASA satellites and other vehicles have survived beyond their expected lifespans
Harsh landing and operational environments
Radiation hardening of circuits
Shielding against radiation
Solar energy (not always available)
Autonomy: signals take a long time to get there
Sleep mode to preserve precious resources
Notes: See NASA’s Web page on the Mars Rovers:
http://mars.jpl.nasa.gov/mer/home/

## Slide 21: Conclusions and the Road Ahead
Information systems are everywhere
  We are dependent on them
  Feel powerless when we lose access
  Yet we can’t quite trust them
Self-x has both positive and negative aspects
  Self-organizing: What are the objectives?
  Self-improving: Who sets the values?
  Self-healing: What if the system mutates?
  Self-sustaining: Can we still pull “the plug”?
B. Parhami
Engineering the Future
Slide # 021
Notes: We have made good progress in technical dimensions for achieving the four “self-x” notions discussed in this talk. The social and ethical dimensions need more work and must be given high priority.

## Slide 22: Questions or Comments?
parhami@ece.ucsb.edu
http://www.ece.ucsb.edu/~parhami/
?
?
?
?
?
B. Parhami
Engineering the Future
Slide # 022