## Slide 1: 100-340GHz wireless communications and imaging
Microelectronics Reliability and Qualification Workshop, The Aerospace Corporation, El Segundo, CA, Feb. 5-7, 2019
M. Rodwell, UC Santa Barbara ; A. Niknejad, UC Berkeley;
J. Buckwalter, U. Madhow, U. Mishra, S. Stemmer, UC Santa Barbara; E. Alon, B. Nikolic, V. Stojanovic, UC Berkeley; D. Jena, A. Molnar, C. Studer, H. Xing, Cornell; A. Molisch, H. Hashemi, USC; H. Krishnaswamy, Columbia; G. Rebeiz, UC San Diego; D. Katabi, MIT; S. Rangan, NYU; A. Arbabian, Stanford; S. Chowdhury, UC Davis; K. O, UT Dallas
This work was supported in part by the Semiconductor Research Corporation (SRC) and DARPA.

## Slide 2: Why 100-340GHz wireless ?
Wireless networks: exploding demand.
Immediate industry response: 5G. 28, 38, 57-71(WiGig), 71-86GHz increased spectrum, extensive beamforming
Next generation (6G ??): above 100GHz. greatly increased spectrum, massive spectral multiplexing
Also TV-like imaging/sensing/radar: cars, airplanes, drones

## Slide 3: 100-340GHz: high-capacity communications
Gigabit mobile communication: Information anywhere, any time, without limits
Residential/office communication: Cellular/internet convergence: competition, low cost, broader deployment

## Slide 4: 100-340GHz imaging: fog/clouds/smoke/dust

## Slide 5: 100-340GHz: benefits & challenges

## Slide 6: 140-340GHz: ComSenTer target applications
MIMO hub: 128 beams/face, 1/10Gb/s/user 140 GHz
Point-point MIMO: 340GHz: Tb/s links massive spatial multiplexing
220, 340GHz imaging: drive/fly in fog/rain/snow 300m, 512×64 image, 60Hz, 15dB SNR
Ultra-compact imaging: drones unlike visible: image through fog/smoke/rain

## Slide 7
140-340 GHz: Applications

## Slide 8: 140 GHz spatially multiplexed base station
1 Tb/s spatially-multiplexed base station 256 users/face, 4 faces 1024 total users @ 1 user/beam, 1 Gb/s/beam; 225 m range
Link budget is feasible, but... Required component dynamic range ? Required complexity of back-end beamformer ?
Handset: 8 × 8 array (9×9mm)

## Slide 9: 140 GHz spatially multiplexed base station
Each face supports 256 beams @ 1Gb/s/beam.
225 meters range in 50 mm/hr rain
PAs: 16 dBm Pout (per element)
LNAs: 3 dB noise figure
Realistic packaging loss, operating & design margins (20dB total)

## Slide 10: 75 GHz spatially multiplexed base station
Suppose we instead use a 75GHz carrier: keep the handset the same size: 8mm×8mm (4×4) keep the same # base station array elements → same Friss transmission losses Also: same 4-9's foul-weather losses
Then: almost the same range (210 meters vs. 225 meters) larger array dimensions 9mm×655mm (vs. 5mm×350mm)
but, today 75GHz ICs are easier than 140GHz ICs…

## Slide 11: 340 GHz (or even 650 GHz) backhaul
Sub-mm-wave line-of-sight MIMO network backbone wireless @ optical speed; link network where fiber is too expensive to place. 340 GHz: 640Gb/s @ 500 meters range; 1.6 meter linear array (5Tb/s for 8×8 square array). 650 GHz: 1.28Tb/s @ 500 meter range; 1.6 meter linear array. Capacity doubles again if we use both polarizations.
linear array
square array

## Slide 12: 340 GHz 640 Gb/s MIMO backhaul
1.6m MIMO array: 8-elements, each 80 Gb/s QPSK; 640Gb/s total 4 × 4 sub-arrays → 8 degree beamsteering
500 meters range in 50 mm/hr rain; 29 dB/km
PAs: 82mW Pout (per element)
LNAs: 4 dB noise figure
Realistic packaging loss, operating & design margins

## Slide 13: 340 GHz 5 Tb/s MIMO backhaul
8-element 640Gb/s linear array: requires 80mW power/element requires 1.6m linear array
8-element 5Tb/s square array: same link assumptions requires 10mW power/element ...10W total radiated power requires 1.6m square array
500m range in 50mm/hr. rain.

## Slide 14: 340 GHz frequency-scanned imaging car radar
Imaging for cars, aircraft drive safely @ 65MPH in heavy fog fly in heavy dust/fog/smoke
Short wavelengths: HDTV-resolution imaging, small: helicopter, drone, car
The challenge: complexity standard array: # pixels = # RF channels HDTV image: ~2×106 pixels. Need 2×106 RF channels !
Hardware-efficient imaging # RF channels << # pixels several techniques

## Slide 15: 340 GHz frequency-scanned imaging car radar
Image refresh rate: 60 Hz
Resolution 64×512 pixels
Angular resolution: 0.14 degrees
Aperture: 35 cm by 35 cm
Angular field of view: 9 by 73 degrees
Component requirements: 44 mW peak power/element, 3% pulse duty factor 6 dB noise figure, 3 dB package losses (each: trx, rcvr) 5 dB manufacturing/aging margin
See a soccer ball at 300 meters in heavy fog (10 seconds warning @ 100 km/hr.) (5 dB SNR, 35 dB/km, 30cm diameter target, 10% reflectivity)

## Slide 16
Transistors

## Slide 17: mm-Wave Wireless Transceiver Architecture
custom PAs, LNAs → power, efficiency, noise Si CMOS beamformer→ integration scale
...similar to today's cell phones.

## Slide 18: 100-1000 GHz transistors and ICs
 | fmax GHz | Good ICs to (GHz) | complexity | LNAs | PAS | increased bandwidth ?
CMOS | 350 | 150/200 | multichannel transceivers | ok | poor: 1-5 mW | not looking good
Production SiGe | 300 | 200/250 | multichannel transceivers | good | OK: 20-100 mW | depends on $$
R&D SiGe | 700 | 300/500 | multichannel transceivers | good | OK: 20-100 mW | 2-3THz
R&D InP HBT | 1150 | 400/650 | PA, frequency converters | poor | good: 100-200 mW | 2-3THz
R&D InP HEMT | 1500 | 500/1000 | LNA | great | weak: 20-50 mW | 2-3THz
R&D GaN | 400 | 120/140 | PAs | good | excellent: 0.1-1W | 600GHz
CNT, 2D, plasmonics etc. : no evidence or theory suggesting that these are useful or superior for 100-2000GHz ICs with useful performance, hero experiments |  |  |  |  |  | 
THz transistors exist today; further R&D will further extend their bandwidth The challenge: driving the (reduced cost→ larger market→ reduced cost) cycle

## Slide 19: 130nm / 1.1THz InP HBT Technology
Teledyne: M. Urteaga et al: 2017 IEEE Proceedings
Integrated ~600GHz transmitter
220 GHz, 0.18W power amplifier
UCSB/Teledyne: T. Reed et al: 2013 CSICS
325 GHz, 16mW power amplifier
UCSB/Teledyne: A. Ahmed, 2018 EuMIC Symp.
1.1THz fmax HBT, 3.5 V breakdown
Teledyne/UCSB: M. Urteaga et al: 2011 DRC

## Slide 20: Challenges at the 64nm/2THz & 32nm/3THz Nodes
Baraskar et al, Journal of Applied Physics, 2013
Need high base contact doping >1020/cm3 for good contacts high Auger recombination very low b.
Need moderate contact penetration Pd or Pt contacts react with 3++ nm of base penetrate surface contaminants too deep for thin base
Solution: base regrowth: thin, moderately-doped intrinsic base thick, heavily-doped extrinsic base
Rode et al., IEEE TED, Aug. 2015

## Slide 21: FETs (HEMTs): key for low noise
2:1 to 4:1 increase in ft : improved noise less required transmit power smaller PAs, less DC power
or higher-frequency systems
Xiaobing Mei, et al, IEEE EDL, April 2015 (Northrop-Grumman)
First Demonstration of Amplification at 1 THz Using 25-nm InP High Electron Mobility Transistor Process

## Slide 22
Towards faster HEMTs: MOS-HEMTs
Scaling limit: gate insulator thickness HEMT: InAlAs barrier: tunneling, thermionic leakage solution: replace InAlAs with high-K dielectric 2nm ZrO2 (er=25): adequately low leakage
Scaling limit: source access resistance HEMT: InAlAs barrier is under N+ source/drain solution: regrowth, place N+ layer on InAs channel Target ~10nm node ~0.3nm EOT, 3nm thick channel 1.2 to 1.5 THz ft.
Jun Wu, UCSB, IEEE EDL, 2018
1st demonstration: Fraunhofer IAF

## Slide 23
ICs

## Slide 24: 130nm /1.1 THz InP HBT ICs to 670 GHz
614 GHz fundamental VCO
340 GHz dynamic frequency divider
620 GHz, 20 dB gain amplifier
M Seo, TSC IMS 2013
also: 670GHz amplifier J. Hacker , TSC IMS 2013 (not shown)
M. Seo, TSC / UCSB
M. Seo, UCSB/TSC IMS 2010
204 GHz static frequency divider (ECL master-slave latch)
Z. Griffith, TSC / UCSB CSIC 2010
300 GHz fundamental PLL
M. Seo, TSC IMS 2011
220 GHz 180 mW power amplifier
T. Reed, UCSB CSICS 2013
600 GHz Integrated Transmitter PLL + Mixer
M. Seo TSC
Integrated 300/350GHz Receivers: LNA/Mixer/VCO
M. Seo TSC
81 GHz 470 mW power amplifier
H-C Park UCSB IMS 2014
530 GHz dynamic frequency divider
M. Seo, TSC IEICE letter 2015
94 GHz ultra low power phased-array pixel
S-K. Kim, UCSB IEEE JSSC 2017

## Slide 25: 140GHz MIMO transceiver front-end ICs
S. Lee, A. Simseck, UCSB, 2018 BCICTS, to be presented

## Slide 26
Systems & Packages

## Slide 27: Beamforming for massive spatial multiplexing
Pure digital beamforming: dynamic range & phase noise requirements: both appear to be manageable  Digital back-end processing requirements (die area, DC power): being investigated ???
Pure RF beamforming: (focal plane, Butler matrixes, RF beamforming) Established approach in DOD systems (high dynamic range). Issues of array tiling.

## Slide 28: The mm-wave module design problem
How to make the IC electronics fit ? l0/2 spacing= 1mm @ 150GHz How to fit large power amplifier die ? Catastrophic losses ? Wire bonds, flip-chip bonds If large apertures, losses on any long interconnects
How to remove the heat ? High power densities

## Slide 29: mm-wave/sub-mm-wave packaging
Not all systems steer in two planes... ...some steer in only one.
Not all systems steer over 180 degrees... ...some steer a smaller angular range
Arrays can often be linear (1D), instead of rectangular (2D) Element spacing can often be greater than l/2.
→ Array packaging then greatly simplified.

## Slide 30
Wireless above 100GHz

## Slide 31: Wireless above 100 GHz
Massive capacities large available bandwidths massive spatial multiplexing in base stations and point-point links
Very short range: few 100 meters short wavelength, high atmospheric losses. Easily-blocked beams.
IC Technology All-silicon for short ranges below 250 GHz. III-V LNAs and PAs for longer-range links. Just like cell phones today III-V frequency extenders for 340GHz and beyond
The challenges spatial multiplexing: computational complexity, dynamic range packaging: fitting signal channels in very small areas

## Slide 32
In case of questions

## Slide 33: Concept: Tile for linear arrays
Terrestrial system: horizontal steering only→ linear array. Space at edges of linear array: room for III-V PAs, LNAs. Alternating-sides feed: 2mm pitch→ room for large GaN PAs. Mounting directly on metal carrier→ heatsinking.

## Slide 34: 140 GHz, 640 Gb/s MIMO backhaul
8-element 640Gb/s linear array: same link assumptions requires 2mW (vs. 80mW) power/element requires 2.6m (vs. 1.6m) linear array
Why not use a lower-frequency carrier, e.g. 140 GHz ?
8-element 5Tb/s square array: same link assumptions requires 0.25mW (vs. 10mW) power/element requires 2.6m (vs. 1.6m) square array

## Slide 35: 140 GHz spatially multiplexed base station

## Slide 36: 75 GHz spatially multiplexed base station
If we use instead a 75GHz carrier, the range increases to 325 meters (vs. 250 meters) but the handset becomes 16mm×16mm (vs. 9mm×9mm), and the hub array becomes 9mm×655mm (vs. 5mm×350mm)
Or, use a 4×4 (8mm×8mm) handset array, and the range becomes 210 meters.

## Slide 37: 340 GHz 640 Gb/s MIMO backhaul

## Slide 38: 340 GHz 5 Tb/s MIMO backhaul
requires 10mW output per element ...10W total radiated power

## Slide 39: Background: split-block waveguides
Waveguides are manufactured (milled or die cast) from a set of pieces
Precision pins aid alignment

## Slide 40: Concept: Tile for mm-wave arrays
Split-block assembly. Modules tile into larger array
IC area can be much larger than antenna area→ electronics can fit
Low-loss waveguide feeds, efficient waveguide horn antennas
Efficient heat-sinking: permits W-level GaN, InP, SiGe PAs for long range

## Slide 41: Concept: Tile for linear arrays
Terrestrial system: horizontal steering only→ linear array. Space at edges of linear array: room for III-V PAs, LNAs. Alternating-sides feed: 2mm pitch→ room for large GaN PAs. Mounting directly on metal carrier→ heatsinking.

## Slide 42: Concept: module for small angular scanning
Terrestrial system: horizontal + vertical steering → rectangular array. Limited angular steering range (installation)→ spacing >> l/2 Endfire / edge-card geometry: room for III-V PAs, LNAs. Mounting directly on metal carrier→ heatsinking.
If Vivaldi's are replaced with dipoles, element spacing can be reduced to l/2. → potential for wider angular scanning

## Slide 43: Concept: module for handset
Handset transceiver performance: less challenging. No external III-V PAs, LNAs
Handset transceiver is simpler: single-beam, not spatially multiplexed Smaller die area→ array pixel fits in l/2 × l/2
Vertical integration of antenna on low-er superstrate. fused Silica (Rebeiz) possibly also: spin-cast BCB or polyimide, post-process.

## Slide 44: Gallium Nitride Power Technologies
N-polar GaN: Mishra
GaN is the leading high-frequency power technology