## Slide 1: 100-300GHz Wireless Communications: Systems, Arrays, ICs, and Transistors
This work was supported in part by the Semiconductor Research Corporation (SRC) and DARPA.
2021 Joint EuCNC & 6G Summit, June 8-11, 2021 (online meeting)
Mark Rodwell,University of California, Santa Barbara, rodwell@ece.ucsb.edu Ali Niknejad, University of California, Berkeley
Debdeep Jena, Alyosha Molnar, Christoph Studer, Huili Xing: Cornell University Muhannad Bakir: Georgia Tech Sundeep Rangan: New York University Amin Arbabian, Srabanti Chowdhury: Stanford Elad Alon, Ali Niknejad, Borivoje Nikolic : University of California, Berkeley Danijela Cabric, Tim Fisher: University of California, Los Angeles Andrew Kummel, Gabriel Rebeiz: University of California, San Diego Jim Buckwalter, Upamanyu Madhow, Umesh Mishra, Mark Rodwell, Susanne Stemmer: University of California, Santa Barbara Andreas Molisch: University of Southern California Kenneth O: University of Texas, Dallas

## Slide 2: Collaborators (ComSenTer Wireless Team)
Elad Alon
UC Berkeley
Upamanyu
Madhow
UC Santa Barbara
James Buckwalter
UC Santa Barbara
Systems
Borivoje Nikolic
UC Berkeley
Ali Niknejad
UC Berkeley
Umesh Mishra
UC Santa Barbara
Srabanti Chowdhury
UC Davis
Gabriel Rebeiz
UC San Diego
Sundeep
Rangan
Susanne Stemmer
UC Santa Barbara
ICs
Transistors
N-polar GaN HEMTs for 140, 210GHz
AlN/GaN HEMTs for 140, 210GHz
GaN HEMTs on Si
Diamond cooling for GaN
Networks, Applications, MIMO, Power
MIMO algorithms Imaging algorithms Compressive imaging
MIMO algorithms VLSI MIMO digital beamforming
mm-wave CMOS: hub mm-wave arrays mm-wave MIMO
mm-wave CMOS: handset mm-wave arrays
efficient PAs III-V arrays
Kenneth O
UT Dallas
Alyosha Molnar
Cornell
Debdeep Jena
Cornell
Huili (Grace) Xing
Cornell
Christoph Studer
Cornell
Amin Arbabian
Stanford
Andreas Molisch
USC
N-path mixers MIMO ADCs
140-300GHz SiGe ICs
design automation equalizers
transistors in novel materials
100-300GHz propagation measurements
advanced packaging materials
VLSI design automation VLSI MIMO processors
140GHz radar chipsets and arrays
Massive MIMO demo.
Compressive imaging
Mark Rodwell
UC Santa Barbara
THz HBTs for PAs THz HEMTs for LNAs
140/210/280GHz arrays for demos.
Danijela Cabric
UCLA
Tim Fisher
UCLA
high- frequency packaging
advanced packaging materials
Muhannad Bakir Georgia Tech
Andrew Kummel
UCSD
MIMO algorithms (funding via CONIX)

## Slide 3: Sponsors

## Slide 4: Beyond-5G Wireless
ComSenTer: 100-300GHz carriers, massive spatial multiplexing → Terabit hubs and backhaul links, high-resolution imaging radar
Wireless networks: exploding demand.
Immediate industry response: 5G. ~10-100GHz carriers. increased spectrum, extensive beamforming
Next generation (6G ??): above 100GHz.. greatly increased spectrum, massive spatial multiplexing
JUMP Centers: research commercialized in 15 years

## Slide 5: Benefits of Short Wavelengths
Communications: Massive spatial multiplexing, massive # of parallel channels. Also, more spectrum!
Imaging: very fine angular resolution
But: High losses in foul or humid weather. High l2/R2 path losses. ICs: poorer PAs & LNAs. Beams easily blocked.
100-340GHz wireless: terabit capacity, short range, highly intermittent

## Slide 6: Potential 100-300GHz Systems
140GHz MIMO Hub
210 or 280GHz MIMO Backhaul
140 or 210GHz Imaging Radar

## Slide 7: 140GHz massive MIMO hub
0.5-5 Tb/s spatially-multiplexed 140GHz base station 128 users/face, 4 faces. P1dB=21 dBm PAs, F=8dB LNAs 512 total users @ 1 user/beam, 1,10 Gb/s/beam; 230, 100 m range in 50mm/hr rain with 17dB total margins
Handset: 8 × 8 array (9×9mm)

## Slide 8: 140GHz moderate-MIMO hub
If demo uses 32-element array (four 1×8 modules): 16 users/array. P1dB=21 dBm PAs, F=8dB LNAs 1,10 Gb/s/beam→ 16, 160 Gb/s total capacity 40, 70 m range in 50mm/hr rain with 17dB total margins
Range varies as (# hub elements)0.5 → (Service area/element) is constant
Handset: 8 × 8 array (9×9mm)

## Slide 9: 210 GHz, 640 Gb/s MIMO Backhaul
8-element MIMO array 3.1 m baseline. 80Gb/s/subarray→ 640Gb/s total 4 × 4 sub-arrays → 8 degree beamsteering
Key link parameters 500 meters range in 50 mm/hr rain; 23 dB/km 20 dB total margins: packaging loss, obstruction, operating, design, aging PAs: 18dBm =P1dB (per element) LNAs: 6dB noise figure

## Slide 10: System Design
ADCs/DACs: only 3-4 bit ADC/DACs required (Madhow, Studer, Rodwell)
Linearity: Amplifier P1dB need be only 3dB above average power (Madhow)
Phase noise: Requirements same as for SISO (Alon, Madhow, Niknejad, Rodwell)
Efficient digital beamforming: beamspace algorithm=complexity ~N× log(N) (Madhow, Studer)
Efficient digital beamforming: low-resolution matrix (Studer)
Efficient channel estimation : fast beamspace algorithm (Studer)
Efficiently addressing true-time-delay problem: "rainbow" FFT algorithm (Madhow, Cabric, Studer)

## Slide 11: 100-1000 GHz Transistors and ICs
 | fmax GHz | Good ICs to (GHz) | complexity | LNAs | PAS | increased bandwidth ?
CMOS | 350 | 150/200 | transceivers | good | weak: 10-30 mW | not easy
Production SiGe | 300 | 200/250 | transceivers | ok | OK: 20-100 mW | depends on $$
R&D SiGe | 700 | 300/500 | transceivers | good | OK: 20-100 mW | 2-3THz
R&D InP HBT | 1150 | 400/650 | PA, converters | ok* | good: 100-200 mW | 2-3THz
R&D InP HEMT | 1500 | 500/1000 | LNA | great | weak: 20-50 mW | 2-3THz
R&D GaN | 400 | 120/140 | PAs | good | excellent: 0.1-1W | 600GHz
ICs with useful performance, hero experiments *can be addressed |  |  |  |  |  | 
There are THz transistors today; their bandwidth will increase
Challenge: reducing costs, increasing market size

## Slide 12: The mm-wave module design problem
How to make the IC electronics fit ? How to avoid catastrophic signal losses ? How to remove the heat ?
Not all systems steer in two planes... ...some steer in only one.
Not all systems steer over 180 degrees... ...some steer a smaller angular range

## Slide 13: 140GHz hub: packaging challenges
IC-package interconnects Difficult at > 100 GHz
Removing heat Thermal vias are marginal
Interconnect density Dense wiring for DC, LO, IF, control. Hard to fit these all in.
Economies of scale Advanced packaging standards require sophisticated tools High-volume orders only Hard for small-volume orders (research, universities) Packaging industry is moving offshore

## Slide 14: 140GHz hub: ICs & Antennas
110mW InP Power Amplifier 20.8% PAE
190mW InP Power Amplifier 16.7% PAE
CMOS Transmitter IC 22nm SOI CMOS.
Receiver IC 22nm SOI CMOS.
LTCC Array module
1 cm
Teledyne InP HBT
GlobalFoundries 22nm SOI CMOS
Kyocera

## Slide 15: 8-Channel 140GHz MIMO hub modules being tested.

## Slide 16: ICs for 210GHz and 280GHz MIMO links
210GHz and 280GHz transceivers in development.
210GHz transmitter, receiver: M. Seo et al, 2021 IMS
200GHz high-efficiency power amplifier: A. Ahmed et al, 2021 IMS
270GHz high-efficiency power amplifier: A. Ahmed et al, 2021 RFIC
4-channel 210GHz tranmistter and receiver arrays: to be tested
280GHz transmitter and receiver ICs: being designed.

## Slide 17: A few key IC results
IMS2021, RFIC201, JSSC submission
ISSCC2021
IMS2021, RFIC2021, IMS2020, EuMIC2020, RFIC2019, EuMIC2021 submission

## Slide 18: Wireless above 100 GHz
Massive capacities large available bandwidths massive spatial multiplexing in base stations and point-point links
Very short range: few 100 meters short wavelength, high atmospheric losses. Easily-blocked beams.
IC Technology All-CMOS for short ranges below 200 GHz. SiGe, GaN, or III-V LNAs and PAs for longer-range links. Just like cell phones today SiGe or III-V frequency extenders for 220GHz and beyond
The challenges digital beamformer computational complexity packaging: fitting signal channels in very small areas mesh networking to accommodate beam blockage driving the technologies to low cost

## Slide 19
(backup files follow)

## Slide 20: 100-300GHz Wireless Communications: Systems, Arrays, ICs, and Transistors
This work was supported in part by the Semiconductor Research Corporation (SRC) and DARPA.
2021 Joint EuCNC & 6G Summit, June 8-11, 2021 (online meeting)
Mark Rodwell, University of California, Santa Barbara, rodwell@ece.ucsb.edu
Debdeep Jena, Alyosha Molnar, Christoph Studer, Huili Xing: Cornell University Muhannad Bakir: Georgia Tech Sundeep Rangan: New York University Amin Arbabian, Srabanti Chowdhury: Stanford Elad Alon, Ali Niknejad, Borivoje Nikolic : University of California, Berkeley Danijela Cabric, Tim Fisher: University of California, Los Angeles Andrew Kummel, Gabriel Rebeiz: University of California, San Diego Jim Buckwalter, Upamanyu Madhow, Umesh Mishra, Mark Rodwell, Susanne Stemmer: University of California, Santa Barbara Andreas Molisch: University of Southern California Kenneth O: University of Texas, Dallas

## Slide 21: Collaborators (ComSenTer Wireless Team)
Elad Alon
UC Berkeley
Upamanyu
Madhow
UC Santa Barbara
James Buckwalter
UC Santa Barbara
Systems
Borivoje Nikolic
UC Berkeley
Ali Niknejad
UC Berkeley
Umesh Mishra
UC Santa Barbara
Srabanti Chowdhury
UC Davis
Gabriel Rebeiz
UC San Diego
Sundeep
Rangan
Susanne Stemmer
UC Santa Barbara
ICs
Transistors
N-polar GaN HEMTs for 140, 210GHz
AlN/GaN HEMTs for 140, 210GHz
GaN HEMTs on Si
Diamond cooling for GaN
Networks, Applications, MIMO, Power
MIMO algorithms Imaging algorithms Compressive imaging
MIMO algorithms VLSI MIMO digital beamforming
mm-wave CMOS: hub mm-wave arrays mm-wave MIMO
mm-wave CMOS: handset mm-wave arrays
efficient PAs III-V arrays
Kenneth O
UT Dallas
Alyosha Molnar
Cornell
Debdeep Jena
Cornell
Huili (Grace) Xing
Cornell
Christoph Studer
Cornell
Amin Arbabian
Stanford
Andreas Molisch
USC
N-path mixers MIMO ADCs
140-300GHz SiGe ICs
design automation equalizers
transistors in novel materials
100-300GHz propagation measurements
advanced packaging materials
VLSI design automation VLSI MIMO processors
140GHz radar chipsets and arrays
Massive MIMO demo.
Compressive imaging
Mark Rodwell
UC Santa Barbara
THz HBTs for PAs THz HEMTs for LNAs
140/210/280GHz arrays for demos.
Danijela Cabric
UCLA
Tim Fisher
UCLA
high- frequency packaging
advanced packaging materials
Muhannad Bakir Georgia Tech
Andrew Kummel
UCSD
MIMO algorithms (funding via CONIX)

## Slide 22: Sponsors

## Slide 23: Beyond-5G Wireless
ComSenTer: 100-300GHz carriers, massive spatial multiplexing → Terabit hubs and backhaul links, high-resolution imaging radar
Wireless networks: exploding demand.
Immediate industry response: 5G. ~10-100GHz carriers. increased spectrum, extensive beamforming
Next generation (6G ??): above 100GHz.. greatly increased spectrum, massive spatial multiplexing
JUMP Centers: research commercialized in 15 years

## Slide 24: Benefits of Short Wavelengths
Communications: Massive spatial multiplexing, massive # of parallel channels. Also, more spectrum!
Imaging: very fine angular resolution
But: High losses in foul or humid weather. High l2/R2 path losses. ICs: poorer PAs & LNAs. Beams easily blocked.
100-340GHz wireless: terabit capacity, short range, highly intermittent

## Slide 25: Potential 100-300GHz Systems
140GHz MIMO Hub
210 or 280GHz MIMO Backhaul
140 or 210GHz Imaging Radar

## Slide 26: 140GHz massive MIMO hub
0.5-5 Tb/s spatially-multiplexed 140GHz base station 128 users/face, 4 faces. P1dB=21 dBm PAs, F=8dB LNAs 512 total users @ 1 user/beam, 1,10 Gb/s/beam; 230, 100 m range in 50mm/hr rain with 17dB total margins
Handset: 8 × 8 array (9×9mm)

## Slide 27: 140GHz moderate-MIMO hub
If demo uses 32-element array (four 1×8 modules): 16 users/array. P1dB=21 dBm PAs, F=8dB LNAs 1,10 Gb/s/beam→ 16, 160 Gb/s total capacity 40, 70 m range in 50mm/hr rain with 17dB total margins
Range varies as (# hub elements)0.5 → (Service area/element) is constant
Handset: 8 × 8 array (9×9mm)

## Slide 28: 210 GHz, 640 Gb/s MIMO Backhaul
8-element MIMO array 3.1 m baseline. 80Gb/s/subarray→ 640Gb/s total 4 × 4 sub-arrays → 8 degree beamsteering
Key link parameters 500 meters range in 50 mm/hr rain; 23 dB/km 20 dB total margins: packaging loss, obstruction, operating, design, aging PAs: 18dBm =P1dB (per element) LNAs: 6dB noise figure

## Slide 29
Systems

## Slide 30: System Design
ADCs/DACs: only 3-4 bit ADC/DACs required (Madhow, Studer, Rodwell)
Linearity: Amplifier P1dB need be only 3dB above average power (Madhow)
Phase noise: Requirements same as for SISO (Alon, Madhow, Niknejad, Rodwell)
Efficient digital beamforming: beamspace algorithm=complexity ~N× log(N) (Madhow, Studer)
Efficient digital beamforming: low-resolution matrix (Studer)
Efficient channel estimation : fast beamspace algorithm (Studer)
Efficiently addressing true-time-delay problem: "rainbow" FFT algorithm (Madhow, Cabric, Studer)

## Slide 31
Transistors

## Slide 32: 100-1000 GHz Transistors and ICs
 | fmax GHz | Good ICs to (GHz) | complexity | LNAs | PAS | increased bandwidth ?
CMOS | 350 | 150/200 | transceivers | good | weak: 10-30 mW | not easy
Production SiGe | 300 | 200/250 | transceivers | ok | OK: 20-100 mW | depends on $$
R&D SiGe | 700 | 300/500 | transceivers | good | OK: 20-100 mW | 2-3THz
R&D InP HBT | 1150 | 400/650 | PA, converters | ok* | good: 100-200 mW | 2-3THz
R&D InP HEMT | 1500 | 500/1000 | LNA | great | weak: 20-50 mW | 2-3THz
R&D GaN | 400 | 120/140 | PAs | good | excellent: 0.1-1W | 600GHz
ICs with useful performance, hero experiments *can be addressed |  |  |  |  |  | 
There are THz transistors today; their bandwidth will increase
Challenge: reducing costs, increasing market size

## Slide 33
ICs and Packages

## Slide 34: The mm-wave module design problem
How to make the IC electronics fit ? How to avoid catastrophic signal losses ? How to remove the heat ?
Not all systems steer in two planes... ...some steer in only one.
Not all systems steer over 180 degrees... ...some steer a smaller angular range

## Slide 35: 140GHz hub: packaging challenges
IC-package interconnects Difficult at > 100 GHz
Removing heat Thermal vias are marginal
Interconnect density Dense wiring for DC, LO, IF, control. Hard to fit these all in.
Economies of scale Advanced packaging standards require sophisticated tools High-volume orders only Hard for small-volume orders (research, universities) Packaging industry is moving offshore

## Slide 36: 140GHz hub: ICs & Antennas
110mW InP Power Amplifier 20.8% PAE
190mW InP Power Amplifier 16.7% PAE
CMOS Transmitter IC 22nm SOI CMOS.
Receiver IC 22nm SOI CMOS.
LTCC Array module
1 cm
Teledyne InP HBT
GlobalFoundries 22nm SOI CMOS
Kyocera

## Slide 37: 8-Channel 140GHz MIMO hub modules being tested.

## Slide 38: ICs for 210GHz and 280GHz MIMO links
210GHz and 280GHz transceivers in development.
210GHz transmitter, receiver: M. Seo et al, 2021 IMS
200GHz high-efficiency power amplifier: A. Ahmed et al, 2021 IMS
270GHz high-efficiency power amplifier: A. Ahmed et al, 2021 RFIC
4-channel 210GHz tranmistter and receiver arrays: to be tested
280GHz transmitter and receiver ICs: being designed.

## Slide 39: A few key IC results

## Slide 40
100-300GHz Wireless

## Slide 41: Wireless above 100 GHz
Massive capacities large available bandwidths massive spatial multiplexing in base stations and point-point links
Very short range: few 100 meters short wavelength, high atmospheric losses. Easily-blocked beams.
IC Technology All-CMOS for short ranges below 200 GHz. SiGe, GaN, or III-V LNAs and PAs for longer-range links. Just like cell phones today SiGe or III-V frequency extenders for 220GHz and beyond
The challenges digital beamformer computational complexity packaging: fitting signal channels in very small areas mesh networking to accommodate beam blockage driving the technologies to low cost