## Slide 1: 100-300GHz Wireless: Transistors, ICs, packages, systems.
Mark Rodwell, UCSB
6G Workshop, IEEE RF/Wireless Week, January 2021, online.
Harish Krishnaswami: Columbia University Debdeep Jena, Alyosha Molnar, Christoph Studer, Huili Xing: Cornell University Dina Katabi: MIT Sundeep Rangan: New York University Amin Arbabian, Srabanti Chowdhury: Stanford Elad Alon, Ali Niknejad, Borivoje Nikolic, Vladimir Stojanovic: University of California, Berkeley Danijela Cabric: University of California, Los Angeles Gabriel Rebeiz: University of California, San Diego Jim Buckwalter, Upamanyu Madhow, Umesh Mishra, Mark Rodwell, Susanne Stemmer: University of California, Santa Barbara Andreas Molisch, Hossein Hashemi: University of Southern California Kenneth O: University of Texas, Dallas

## Slide 2: Team and their roles
Elad Alon
UC Berkeley
Upamanyu
Madhow
UC Santa Barbara
James Buckwalter
UC Santa Barbara
Systems
Borivoje Nikolic
UC Berkeley
Vladimir
Stojanovic
UC Berkeley
Ali Niknejad
UC Berkeley
Mark Rodwell
UC Santa Barbara
Umesh Mishra
UC Santa Barbara
Srabanti Chowdhury
UC Davis
Gabriel Rebeiz
UC San Diego
Sundeep
Rangan
Susanne Stemmer
UC Santa Barbara
ICs
Transistors
N-polar GaN HEMTs for 140, 210GHz
AlN/GaN HEMTs for 140, 210GHz
GaN HEMTs on Si
Diamond cooling for GaN
Networks, Applications, MIMO, Power
MIMO algorithms Imaging algorithms Compressive imaging
MIMO algorithms VLSI MIMO processors
mm-wave CMOS: hub mm-wave arrays mm-wave MIMO
mm-wave CMOS: handset mm-wave arrays
efficient PAs III-V arrays
Kenneth O
UT Dallas
Dina Katabi
MIT
Harish Krishnaswamy
Columbia
Alyosha Molnar
Cornell
Debdeep Jena
Cornell
Huili (Grace) Xing
Cornell
Christoph Studer
Cornell
Amin Arbabian
Stanford
Andreas Molisch
USC
Hossein Hashemi
USC
N-path mixers MIMO ADCs
200-300GHz passive CMOS
design automation equalizers
photonic links
transistors in novel materials
THz HBTs for PAs THz HEMTs for LNAs
100-300GHz propagation measurements
Applications: VR, cars, …
STAR Novel MIMO
acoustic filters
VLSI design automation VLSI MIMO processors
140GHz radar chipsets and arrays
Massive MIMO demo.
Compressive imaging
140/210/290GHz arrays for demos.
Danijela Cabric
UCLA
MIMO algorithms

## Slide 3: Beyond-5G Wireless
ComSenTer: 100-300GHz carriers, massive spatial multiplexing → Terabit hubs and backhaul links, high-resolution imaging radar
Wireless networks: exploding demand.
Immediate industry response: 5G. ~10-100GHz carriers. increased spectrum, extensive beamforming
Next generation (6G ??): above 100GHz.. greatly increased spectrum, massive spatial multiplexing
JUMP Centers: research commercialized in 15 years

## Slide 4: Benefits of Short Wavelengths
Communications: Massive spatial multiplexing, massive # of parallel channels. Also, more spectrum!
Imaging: very fine angular resolution
But: High losses in foul or humid weather. High l2/R2 path losses. ICs: poorer PAs & LNAs. Beams easily blocked.
100-340GHz wireless: terabit capacity, short range, highly intermittent

## Slide 5
100-300 GHz: Applications

## Slide 6: 100-300GHz: Demonstration Systems
MIMO hub: 140GHz
Point-point MIMO: 210, 280GHz
Cross-linear-array imaging: 210, 280GHz
UCSB FCC permit: 137 +/- 15 GHz, 210 +/- 15 GHz, 280 +/- 15 GHz

## Slide 7: 140GHz massive MIMO hub
0.5-5 Tb/s spatially-multiplexed 140GHz base station 128 users/face, 4 faces. P1dB=21 dBm PAs, F=8dB LNAs 512 total users @ 1 user/beam, 1,10 Gb/s/beam; 230, 100 m range in 50mm/hr rain with 17dB total margins
Handset: 8 × 8 array (9×9mm)

## Slide 8: 70 GHz spatially multiplexed base station
If we use instead a 70GHz carrier, the range increases to 168 meters (vs. 100 meters) but the handset becomes 16mm×16mm (vs. 8mm×8mm), and the hub array becomes 20mm×524mm (vs. 10mm×262mm)
Or, use a 4×4 (8mm×8mm) handset array, and the range becomes ..100 meters.
Same handset area (more handset elements)→ same link budget Easier to obtain license for 140±2.5GHz than 75±2.5GHz

## Slide 9: 140GHz moderate-MIMO hub
If demo uses 32-element array (four 1×8 modules): 16 users/array. P1dB=21 dBm PAs, F=8dB LNAs 1,10 Gb/s/beam→ 16, 160 Gb/s total capacity 40, 70 m range in 50mm/hr rain with 17dB total margins
Range varies as (# hub elements)0.5 → (Service area/element) is constant
Handset: 8 × 8 array (9×9mm)

## Slide 10: 140GHz Architecture (Sketch)
75GHz RF front-ends BWRC
140 GHz hub RF front-ends UCSB
140GHz handset RF front-ends UCSD Beamforming by:
FPGA: demos, algorithms
BWRC Hydra: flexible, general
Custom Si VLSI beamformer ICs in development (BWRC, Cornell)

## Slide 11: 210 GHz, 640 Gb/s MIMO Backhaul
8-element MIMO array 3.1 m baseline. 80Gb/s/subarray→ 640Gb/s total 4 × 4 sub-arrays → 8 degree beamsteering
Key link parameters 500 meters range in 50 mm/hr rain; 23 dB/km 20 dB total margins: packaging loss, obstruction, operating, design, aging PAs: 18dBm =P1dB (per element) LNAs: 6dB noise figure

## Slide 12: 210 GHz, 5.1 Tb/s MIMO backhaul
8-element 640Gb/s linear array: requires 14dBm transmit power/element (Pout) ….3.2W total output power requires 2.1m linear array
500m range in 50mm/hr. rain.
64-element 5Tb/s square array: same link assumptions requires 5dBm transmit power/element (Pout) ….3.2W total output power requires 2.1m square array
Complex system: can we make it cheaply ?

## Slide 13: 70 GHz, 640 Gb/s MIMO backhaul (16QAM)
Why not use a lower-frequency carrier, e.g. 70 GHz ?
8-element 640Gb/s linear array: requires 11dBm transmit power/element (Pout) ….1.7W total output power requires 5.5m linear array
64-element 5Tb/s square array: same link assumptions requires 2dBm transmit power/element (Pout) ….1.7W total output power requires 5.5m square array
Similar RF power output, physically larger

## Slide 14
Transistors

## Slide 15: 100-1000 GHz Transistors and ICs
 | fmax GHz | Good ICs to (GHz) | complexity | LNAs | PAS | increased bandwidth ?
CMOS | 350 | 150/200 | transceivers | good | weak: 10-30 mW | not easy
Production SiGe | 300 | 200/250 | transceivers | ok | OK: 20-100 mW | depends on $$
R&D SiGe | 700 | 300/500 | transceivers | good | OK: 20-100 mW | 2-3THz
R&D InP HBT | 1150 | 400/650 | PA, converters | ok* | good: 100-200 mW | 2-3THz
R&D InP HEMT | 1500 | 500/1000 | LNA | great | weak: 20-50 mW | 2-3THz
R&D GaN | 400 | 120/140 | PAs | good | excellent: 0.1-1W | 600GHz
ICs with useful performance, hero experiments *can be addressed |  |  |  |  |  | 
There are THz transistors today; their bandwidth will increase
Challenge: reducing costs, increasing market size

## Slide 16: mm-Wave CMOS won't scale much further
Gate dielectric can't be thinned → on-current, gm can't increase
Tungsten via resistances reduce the gain
Inac et al, CSICS 2011
Shorter gates give no less capacitance dominated by ends; ~1fF/mm total
Maximum gm, minimum C→ upper limit on ft. about 350-400 GHz.
Present finFETs have yet larger end capacitances

## Slide 17: mm-Wave Transistor Development
THz InP HBTs: State-of-art: 1.1THz fmax @ 130nm node Efficient 100-650GHz power more fmax: more efficient, higher frequencies base regrowth: better contacts→ higher fmax. status: working DC devices; moving to THz
THz InP HEMTs: State-of-art: 1.5THz fmax @ 32nm node Sensitive 100-650GHz low-noise amplifiers more ft: lower noise, higher frequencies high-K gate dielectric → higher ft, fmax
InGaN and GaN HEMTs: High power from 100-340GHz GaN: superior power density at all frequencies UCSB/Mishra: InGaN for increased mobility Cornell/Xing: AlN/GaN/AlN
N-polar GaN: Mishra, UCSB

## Slide 18
ICs

## Slide 19: ComSenTer Research: ICs
140GHz 8-element handset TRX, RCVR arrays and PAs Rebeiz
280GHz CMOS upconvert mixers 420 GHz CMOS receiver O
210GHz InP transceivers and arrays, 210, 280GHz PAs Seo/Rodwell
Hydra digital processor (beamformer) Nikolic
Beamspace digital beamformer Studer/Molnar
60GHz CMOS channel aggregation transceiver Krishnaswamy
Record-PAE Class B 140GHz PAs Buckwalter
Record-PAE Class A 100-200mW 140GHz PAs Rodwell
140GHz CMOS handset ICs Rodwell
Not shown: 140GHz, 210GHz outphasing transmitters Buckwalter mm-wave N-path mixers Molnar GaN active circulators Krishnaswamy 140GHz GaN PAs Buckwalter
75GHz MIMO front-ends Niknejad, Alon, Nikolic

## Slide 20: ComSenTer 140GHz CMOS ICs for hub & handset
1st-generation hub ICs: UCSB
Handset array ICs: UCSD
2nd-generation hub ICs: UC Berkeley
Farid et al, RFIC 2019
Rebeiz group

## Slide 21: ComSenTer 140GHz InP ICs for hub
110mW power amplifier, 20.8% PAE A. Ahmed, IMS 2020
190mW power amplifier, 16.7% PAE A. Ahmed, EuMIC 2020.
Also: "A 130-GHz Power Amplifier in a 250-nm InP Process with 32% PAE" Kang Ning (Buckwalter group) 2020 RFIC symposium

## Slide 22: 210 GHz MIMO backhaul: ICs
Transmitter without PA: 
PA 
Receiver:
Transmitter with PA: ✘
Teledyne 250nm (650GHz) InP HBT.
M. Seo Sungkyunkwan/UCSB A. Ahmed, U. Solyu, M. Rodwell UCSB
LNA

## Slide 23
Packages / array modules

## Slide 24: The mm-wave module design problem
How to make the IC electronics fit ? How to avoid catastrophic signal losses ? How to remove the heat ?
Not all systems steer in two planes... ...some steer in only one.
Not all systems steer over 180 degrees... ...some steer a smaller angular range

## Slide 25: 140GHz hub: packaging challenges
IC-package interconnects Difficult at > 100 GHz
Removing heat Thermal vias are marginal
Interconnect density Dense wiring for DC, LO, IF, control. Hard to fit these all in.
Economies of scale Advanced packaging standards require sophisticated tools High-volume orders only Hard for small-volume orders (research, universities) Packaging industry is moving offshore

## Slide 26: 100-300GHz IC-package connections
type | Frequency | technology | cost | heatsinking
micromachined waveguide interface | 1000 GHz | Research. Cheap one day ? | high ✘ | good
ribbon, mesh bond | 200 GHz | Handcrafted. | high ✘ | good
patch antennas on superstrate | 1000 GHz | Straightforward | low | good
Cu stud flip-chip | >200 GHz | Industry standard | low | ok, marginal for PA ✘
hot vias | 200 GHz | Development | low ? | good
(ball) wirebonds | 100 GHz ✘ | Industry standard | low | good
Deal, IEEE Trans THz, Sept 2011
G. Rebeiz

## Slide 27: 140GHz massive MIMO hub modules
LTCC-based array tile
Kyocera LTCC carrier
connector interface board
140GHz CMOS ICs
transmit
receive
140GHz InP PAs
8 CMOS ICs, 8 InP PAs
connector interface board
Farid, Ahmed, Rodwell, UCSB; Flynn, Dunn, Niknejad, Nikolic, BWRC; Rebeiz, UCSD
Psat ~100mW
…
…

## Slide 28: 140GHz hub: ICs & Antennas
110mW InP Power Amplifier 20.8% PAE
190mW InP Power Amplifier 16.7% PAE
CMOS Transmitter IC 22nm SOI CMOS.
Receiver IC 22nm SOI CMOS.
LTCC Array module
1 cm
Teledyne InP HBT
GlobalFoundries 22nm SOI CMOS
Kyocera
Farid, Ahmed, Rodwell, UCSB; Flynn, Dunn, Niknejad, Nikolic, BWRC; Rebeiz, UCSD

## Slide 29: 140GHz Single-Channel CMOS+InP Transmitter
A. Farid, A. S. Ahmed, UCSB, modules being tested
Farid, Ahmed, Rodwell, UCSB; Flynn, Dunn, Niknejad, Nikolic, BWRC; Rebeiz, UCSD

## Slide 30: Concept: module for small angular scanning
Terrestrial system: horizontal + vertical steering → rectangular array. Limited angular steering range (installation)→ spacing >> l/2 Endfire / edge-card geometry: room for III-V PAs, LNAs. Mounting directly on metal carrier→ heatsinking.

## Slide 31
2D arrays

## Slide 32: The mm-wave module design problem
How to make the IC electronics fit ? How to avoid catastrophic signal losses ? How to remove the heat ?
Not all systems steer in two planes... ...some steer in only one.
Not all systems steer over 180 degrees... ...some steer a smaller angular range

## Slide 33: 100-300GHz: 2D arrays
Single-beam array: 1 PA, one phase-shifter in ~0.36l2
Multi-beam array: 1 PA, one mixer in ~0.36l2
f | 100 | 150 | 200 | 250 | 300 | GHz
l | 3 | 2 | 1.5 | 1.2 | 1 | mm
l/2 | 1.5 | 1 | 0.75 | 0.6 | 0.5 | mm
0.6l | 1.8 | 1.2 | 0.9 | 0.72 | 0.6 | mm

## Slide 34: 100-300GHz, 2D arrays: ICs can fit
LO frequency multiplier 0.58 mm x 0.4 mm
Phase shifter 0.3 mm x 0.4 mm
TX I/Q mixer 0.16mm x 0.08 mm
LO buffer amp. 0.34 mm x 0.18 mm
RX mixer (I or Q) 0.16 mm x 0.11 mm
200GHz 40mW PA 0.56 mm x 0.78 mm
0.6l x 0.6l
200GHz array cell 0.9 mm x 0.9 mm
(layouts are roughly in proportion; may not be in exact scale)
200GHz 2D arrays: ~feasible with present IC blocks.
300GHz 2D arrays: layout compaction: better IC design smaller power amplifiers better wiring

## Slide 35: How should we scale array design at high frequencies ?
(Worst-case atmospheric loss: ~constant over 50-300GHz)
Proposed scaling law | change
carrier frequency | increase 2:1
aperture area | keep constant
total transmit power | keep constant
Implication | change
capacity (# beams·bit rate per beam) | increases 4:1
number elements | increases 4:1
RF power per cm2 aperture area | stays constant
RF power per element | decreases 4:1
IC area/element (tiled array) | decreases 4:1
IC area/element (trayed array) | decreases 2:1
IC power/area (tiled array) | stays constant
IC power/area (trayed array) | decreases 2:1

## Slide 36
Systems

## Slide 37: Beamforming for massive spatial multiplexing
Pure digital beamforming: dynamic range & phase noise requirements: appear to be manageable  Digital back-end processing requirements (die area, DC power): being investigated ?
Analog, hybrid beamforming: Do not appear to significantly improve dynamic range in massive MIMO.

## Slide 38: Progress in System Design
ADCs/DACs: only 3-4 bit ADC/DACs required (Madhow, Studer)
Linearity: Amplifier P1dB need be only 3dB above average power (Madhow).
Phase noise: Requirements same as for SISO (Alon, Madhow, Niknejad, Rodwell)
Efficient digital beamforming: beamspace algorithm (spatial FFT, sparsity) (Madhow, Studer)
Efficient digital beamforming: low-resolution matrix (Studer, Molnar)
Efficient channel estimation : fast beamspace algorithm (Studer)
Efficiently addressing true-time-delay problem: "rainbow" FFT algorithm (Madhow, Cabric)
Digital beamforming:
Other issues:
Propagation models and measurements
Blockage probability, mesh networks, network protocols

## Slide 39: Progress in System Design
ADC resolution: N ADC bits, M antennas, K signals: SNR=6N+1.76+10.log10(M/K) 3 bits, (M/K)=2→ SNR=23 dB. QPSK needs 9.8 dB.
Jammer tolerance: Increase ADC resolution by 1 bit→ Pjammer,max = K.Psignal Maximum jammer power = sum of all user's power.
Phase noise: Phase error sf : SNR= -20.log10(sf)+10.log10(M/K), where MIMO and SISO require similar L(f) .
Beamspace: lower frequencies, many NLOS paths, complicated channel matrix: O(M3) to beamform higher frequencies, few NLOS paths, simpler channel matrix: FFT, O(M.logM) to beamform fewer bits in signal; fewer bits in FFT coefficients.

## Slide 40: Array-beamformer interconnects
(I,Q) links needs 4 (differential IQ) lines/antenna physically large modules. OK DC power/line (few mW)
IF links as in emerging 5G systems needs one IF line/antenna physically much smaller modules small required DC power/line
Required IF signal interface power is very small; low required DC power for line driver.
(I,Q) links
IF links

## Slide 41
100-300GHz Wireless

## Slide 42: Wireless above 100 GHz
Massive capacities large available bandwidths massive spatial multiplexing in base stations and point-point links
Very short range: few 100 meters short wavelength, high atmospheric losses. Easily-blocked beams.
IC Technology All-CMOS for short ranges below 200 GHz. SiGe, GaN, or III-V LNAs and PAs for longer-range links. Just like cell phones today SiGe or III-V frequency extenders for 220GHz and beyond
The challenges digital beamformer computational complexity packaging: fitting signal channels in very small areas mesh networking to accommodate beam blockage driving the technologies to low cost

## Slide 43
(backup files follow)

## Slide 44: 100-300 GHz: challenges & solutions
Need mesh networks
Need large arrays
High attenuation in foul or humid weather

## Slide 45
Towards faster HEMTs: InAs MOS-HEMTs
Goal: Higher ft for lower noise, sensitive receivers 1200 vs. 600GHz ft : 1.5dB better Fmin @ 300GHz. Increased bandwidth by scaling. Scaling limit: gate insulator thickness InAlAs barrier with high-K dielectric
Scaling limit: source access resistance by regrowth, place N+ layer on InAs channel Also: thinner channel, higher barriers, larger electron supply
Present devices: 420GHz ft, 560GHz fmax @ ~20nm Lg Bandwidth limited by gate misalignment Next step: self-aligned process

## Slide 46: Base Regrowth for THz HBTs
Why regrowth ? good contacts: need high base doping under contacts good DC gain : need lower base doping under emitter solution: heavily-doped regrown extrinsic base
Initial ComSenTer HBT work: nm scaling. HBTs with 90nm emitter width.
First regrown-base results: InGaAs base InGaAs intrinsic base. Regrown GaAs extrinsic base Excellent DC characteristics.  But: hydrogen passivation of InGaAs base during regrowth ✘
Second regrown-base results: GaAsSb base GaAsSb: resistance to hydrogen passivation DC results in winter: good DC characteristics Next step: scaled THz device run.

## Slide 47: 100-300GHz tile array
How to make everything fit ? radiated signal: up intense thermal flux: down DC/control/LO/IF lines: laterally
Need dense I/O and heat removal directly under IC → Crystalline SiC or AlN carrier ($$$) → Ceramic SiC or AlN carrier ($$) → LTCC with diamond/silver-filled thermal vias ($)
If RF power density is independent of wavelength, then so will be the temperature rise across the package

## Slide 48: InP ICs for 210GHz Point-Point MIMO
Transceivers & Arrays for 210GHz MIMO links
2/2020 tapeout: 210 GHz TX front-end w/ +20 dBm Psat 210 GHz TX front-end w/ +2 dBm Psat 210 GHz RX front-end 280GHz PAs and LNAs
5/2020 tapeout: Improved 210, 280GHz LNAs and PAs 210 GHz transmitters, receivers using these 2x2 transmitter array with superstrate antenna 2x2 receiver array with superstrate antenna
Seo, UCSB & Sungkyunkwan Univ.; Ahmed, Solyu, Rodwell, UCSB; Li, Zhang, Rebeiz, UCSD
InP IC bonding to patch antenna arrays on quartz. plan: ribbon bonds using wedge bonder
Planned packaging approaches
2x2 array with UCSD SiO2 antenna superstrate simple, expensive in die area limits array size to 2x2 (or 2x4).